## Slide 1: Intermediate x86 Part 3
Xeno Kovah – 2010
xkovah at gmail
Notes: <number>

## Slide 2: All materials are licensed under a Creative Commons “Share Alike” license.
http://creativecommons.org/licenses/by-sa/3.0/
<number>

## Slide 3: Intermission RDTSC
<number>
What’s the time? Time to ReaD (the) Time-Stamp Counter! (I know, it doesn’t even sort of work)
The TSC is a 64bit counter introduced in the Pentium
Set to 0 when processor reset, incremented on each clock cycle thereafter.
Can set a flag (in CR4) so that only Ring 0 can use the instruction (AFAIK no one does this)
Notes: <number>

## Slide 4: RDTSC 2
<number>
Processor families increment the time-stamp counter differently
RDTSC in practice
  Timing code for performance reasons
  Code which checks for the presence of a debugger by timing its own execution
Further reference - Vol. 3b chapter 18.11
Notes: <number>

## Slide 5: Lab: Guestimate.c
<number>
Simple code to use the timestamp counter to time how long it takes to run some code.
Notes: <number>

## Slide 6: Lab: NavelGaze.c
<number>
Code which looks at itself and changes its behavior if it takes too long to execute (e.g. if a breakpoint was set)
Pop quiz hot shot: You gots malware that’s altering its behavior in response to your breakpoints. What do you do? What DO you DO?!?!
Notes: <number>

## Slide 7: Conclusion:
<number>
Human stepping through code easy to detect
  But analyst will hopefully grasp the nature of the timing check, and work around it
IMHO RDTSC less fun than a barrel of monkeys but more fun than a tube sock of scorpions
Notes: <number>

## Slide 8: Interrupts and Exceptions
<number>
“Interrupts and exceptions are events that indicate that a condition exists somewhere in the system, the processor, or within the currently executing program or task that requires the attention of a processor.”
“When an interrupt is received or an exception is detected, the currently running procedure or task is suspended while the processor executes an interrupt or exception handler. When execution of the handler is complete, the processor resumes execution of the interrupted procedure or task.”
“The processor receives interrupts from two sources:
  External (hardware generated) interrupts.
  Software-generated interrupts.”
Vol 3A, Sect 5.1
Notes: <number>
Consider yourself lucky that I didn’t demonstrate an interrupt with a rickroll on the next slide

## Slide 9: Difference between Interrupt and Exception?
<number>
Exceptions typically indicate error conditions, whereas interrupts typically indicate events from external hardware.
  “Exception - E is for error” ;)
Interrupts clear the Interrupt Flag (IF - talked about later), Exceptions do not.
3 categories of exception:
  Fault - recoverable - pushed EIP points to the faulting instruction
  Trap - recoverable - pushed EIP points to the instruction following the trapping instruction
  Abort - unrecoverable - may not be able to save EIP where abort occurred
Vol 3A, Sect 5.5
Notes: <number>
I wish I could have put the elmo picture in here, but stupid powerpoint 2007 doesn’t allow it anymore

## Slide 10: Fault: EIP points at faulting instruction
<number>
“Zis is all YOUR fault!”
EIP
Notes: <number>
http://6.media.tumblr.com/tumblr_kq03c0CxBs1qztjn5o1_500.png

## Slide 11: Trap: EIP points at instruction after the trapping instruction
<number>
Notes: <number>
http://downlode.org/Creative/Writing/Notebook/Illustrations/itsatrap.jpg

## Slide 12: Abort: unrecoverable, may not be able to save EIP…
<number>
EIP
Notes: <number>
http://icanhascheezburger.files.wordpress.com/2008/03/funny-pictures-nasa-launch-abort-spider.jpg

## Slide 13: Saving State
<number>
When it says the current procedure is suspended, what does it actually mean?
Need to save the relevant state for the current activity, so that the state can be restored after processing the interrupt
The hardware itself saves relatively little state to the stack in the event of an interrupt. An interrupt handler on the other hand may choose to store all of the registers so that they can be replaced when the interrupt has been processed,
Notes: <number>

## Slide 14: Stack On Interrupt
<number>
From Vol. 1
(error code is only there if the particular interrupt creates one)
Notes: <number>

## Slide 15: You couldn’t find your handler’s stack with both hands
<number>
A good question (asked by my wife) is: when there is a privilege change how does the hardware find the stack for the interrupt handler in order to push the saved state onto that stack rather than that of the interrupted procedure?
It consults a structure called the Task State Segment (TSS) to find the new SS and ESP it will use.

## Slide 16: A little bit about “tasks”
<number>
The Intel documentation often references the notion of a “task”.
Eventually I decided to remove most of the description of how tasks work, because it is tangential to the more important stuff, and I anticipate a lack of time.
If you’re a conspiracy theorist, you are invited to read Vol 2a, Section 6 to find out “what Xeno doesn’t want you to know!”….But then…that’s just what I’d be expecting, isn’t it?
Anyway, the Task State Segment (TSS) is something which must be used by the OS by virtue of being consulted on privilege changing interrupts, so we’ll at least talk about that.
There’s a dedicated 16 bit Task Register (TR) which holds a segment selector selecting an entry in the GDT of Task Segment type. (Load/store task register with LTR, STR instructions respectivly
The task segment points to the Task State Segment, which is just a large data structure of mostly saved register values.

## Slide 17: TSS
<number>

## Slide 18: !descriptor TSS printing
I added the following commands to the !descriptor windbg plugin
  !descriptor TSS32 <address>
  !descriptor TSS16 <address>
Just reads memory at the given address and prints out value according to the structure definition
Use with !descriptor GDT <index> to find the base address of a GDT descriptor of 16/32 bit TSS type
<number>

## Slide 19: Interrupt Descriptor Table (IDT)
<number>
And array of <= 256 8-byte descriptor entries. 0 through 31 are reserved for architecture-specific exceptions and interrupts. 32-255 are user defined.
While it interacts with segments, you can think of it as being an array of function pointers, and when interrupt n is invoked by software or hardware, execution transfers to the address pointed to by the nthdescriptor in the table.
Notes: <number>

## Slide 20: Meet The Interrupts
<number>
Notes: <number>

## Slide 21: Meet The Interrupts 2
<number>
For lots of details on 0-19, see Vol. 3a Sect. 5.15
Notes: <number>

## Slide 22: The SegFault is a Lie!
On *nix systems when you access somewhere you’re not supposed to, the program will be shut down with the given reason being “Segmentation Fault”
Looking back at the table we see there is no listed Segmentation Fault.
In fact, for most segmentation errors you can get, they will generate a general protection fault
And we know that segmentation isn’t used to protect memory, so usually if you access invalid memory you’re getting a page fault.
The reality of the SegFault is that it’s a unix Signal, SIGSEGV (signal segment violation). But signals are an OS level abstraction, and this “fault” isn’t a x86 fault.
(I would welcome anyone digging into a *nix and confirming that things like page faults and general protection faults get turned into things like SIGSEGV signals)
<number>

## Slide 23: Software-Generated Interrupts
<number>
INT n - Invoke IDT[n]
  Important: While you can invoke anything in the IDT, some interrupts expect an error code. INT does not push any error code, and therefore a handler may not behave correctly.
  Interrupts generated in software with the INT n instruction cannot be masked by the IF flag in the EFLAGS register. (Talked about later)
IRET - returns from an interrupt, popping all the saved state back into the correct registers
INT 3 - The special 0xCC opcode form of this has an extra caveat that when hardware virtualization is used, it doesn’t intercept this interrupt like it would do with others, and just passes it to the OS debug interrupt handler
INTO - Invoke overflow interrupt if the overflow flag (OF) in EFLAGS is set to 1 (like a conditional INT 4)
UD2 - Invoke invalid opcode interrupt (same as INT 6)
Notes: <number>

## Slide 24: Lab: TryToRunTryToHide.c BreakOnThruToTheOtherSide.c
<number>
Taking a look at what changes and what doesn’t when jumping from userspace to kernel via a software interrupt
Showing the kernel stack values being derived from the TSS
Using rootkit hooking technique you’re not expected to understand yet to intercept the interrupt ;)
Notes: <number>

## Slide 25: Changed Register Results (everything else that we were watching was the same except eip obviously)
Userspace | Kernel
CS = 0x1B | CS = 0x08
SS = 0x23 | SS = 0x10
FS = 0x3B | FS = 0x30
ESP = 0x12FDDC | ESP = 0xF7A2ADCC
EFLAGS:IF = 1 | EFLAGS:IF = 0
<number>

## Slide 26: How is the IDT found?
There is a specific register which points at the base (0th entry) of the IDT. The IDT Register is named IDTR ;)
When interrupt/exception occurs, the hardware automatically
  consults the IDTR
  finds the appropriate offset in the IDT
  pushes the saved state onto the stack
  changes EIP to the address of the interrupt handler, as read from the IDT entry (interrupt descriptor).
<number>

## Slide 27: IDTR Format
<number>
The upper 32 bits of the register specify the linear address where the IDT is stored. The lower 16 bits specify the size of the table in bytes.
Special instructions used to load a value into the register or store the value out to memory
  LIDT - Load 6 bytes from memory into IDTR
  SIDT - Store 6 bytes of IDTR to memory
Structured the same way as the GDT
Also, WinDbg displays upper 32 bits as idtr, and lower parts as idtl.
From Vol 3a.
Figure 2-5
Notes: <number>

## Slide 28: IDTR Usage
<number>
Notes: <number>

## Slide 29: Interrupt Descriptors
<number>
The descriptors in the IDT describe one of three gate types
  Trap Gate
  Task Gate
  Interrupt Gate
“The only difference between an interrupt gate and a trap gate is the way the processor handles the IF flag in the EFLAGS register.“ Discussed later, but from this you can infer that a Trap Exception isn’t related to a Trap Gate. Since there’s the difference between where EIP points for trap vs interrupt exceptions.
Gates are used in the IDT to facilitate control flow transfers between privilege levels
Notes: <number>

## Slide 30: Task Gate Descriptor
<number>
Descriptors not in use should have P = 0
As I said before, I’m not really going to talk about
tasks. But as you can see their gate descriptors
are booooorrrrriiiinnnggggg!

## Slide 31: Interrupt Gate Descriptor
<number>
Note that the two halves
of the offset form a
32 bit address.
Descriptors not in use should have P = 0
Notes: <number>

## Slide 32: Trap Gate Descriptor
<number>
Note that the two halves
of the offset form a
32 bit address
Descriptors not in use should have P = 0
Blink and you’ll miss it…if you’re unable to see red ovals after having blinked. The format is the same except for one bit.
Notes: <number>

## Slide 33: Descriptor Descriptions
The DPL is again the Descriptor Privilege Level. And it is only checked when a descriptor is accessed by a software interrupt, in which case it is only allowed if CPL <= DPL (ignored on hardware interrupts)
Note that the descriptor specifies a segment selector and 32 bit address. Why that looks like a “logical address” aka “far pointer” to me!
D flag specifies whether you’re jumping into a 16 or 32 bit segment.
P (Present) flag
<number>

## Slide 34: IDT Relation to Segments
<number>
Notes: <number>

## Slide 35: Lab: Pearly Gates
<number>
We can take a look at what types of gates are used in the IDT by using this new command I added to the descriptor plugin:
!descriptor IDT
!descriptor IDT_FULL
!descriptor DUMP_IDT_TYPES
Can also use the built in !idt and !idt –a commands
Notes: <number>

## Slide 36: Interrupt Masking
<number>
It is sometimes useful to disable some interrupts. This is called “masking” the interrupt.
The Interrupt Flag (IF) in the EFLAGS register is cleared automatically whenever an interrupt occurs through an interrupt gate (but not a trap gate).
Maskable interrupts can be manually masked by clearing IF. IF can be cleared with the CLI instruction, or set with STI (both ring-0-only instructions). But only if you have sufficient privileges (talked about later)
Notes: <number>

## Slide 37: Interrupt Masking Exceptions
<number>
The IF does not mask the explicit invocation of an interrupt with the INT instruction
The IF does not mask a Non Maskable Interrupt - IDT[2] (duh ;))
Notes: <number>

## Slide 38: Red Pill
<number>
Joanna Rutkowska, 2004 - “Red Pill... or how to detect VMM using (almost) one CPU instruction” http://www.invisiblethings.org/papers/redpill.html
Using SIDT (Store Interrupt Descriptor Table Register) instruction to profile the current value in the IDTR
She had found that the most significant byte of the IDTR had a predictable value in VMWare 4 and VirtualPC, which was different from what it was in an unvirtualized system
Notes: <number>

## Slide 39: Lab: VerboseRedPill.c
As opposed to:
int swallow_redpill () {
unsigned char m[2+4], rpill[] = "\x0f\x01\x0d\x00\x00\x00\x00\xc3";
*((unsigned*)&rpill[3]) = (unsigned)m;
((void(*)())&rpill)();
return (m[5]>0xd0) ? 1 : 0;
}
<number>

## Slide 40: Red Pill 2
<number>
The fundamental problem is that while LIDT is a privileged instruction (requires Ring 0), SIDT is not (and probably should be).
For more examples of why x86 as a platform is not meant to be transparently virtualized see these:
  Analysis of the Intel Pentium’s Ability to Support a Secure Virtual Machine Monitor http://www.cs.nps.navy.mil/people/faculty/irvine/publications/2000/VMM-usenix00-0611.pdf
  Compatibility is Not Transparency: VMM Detection Myths and Realities http://www.stanford.edu/~talg/papers/HOTOS07/vmm-detection-hotos07.pdf
Implication is that malware can detect if it’s being virtualized…but…as more hosts are virtualized, there’s disincentive for malware to not run in virtualized environments.
Notes: <number>

## Slide 41: Ironic Table
<number>

## Slide 42: Stray Instructions Adopted Along The Way
<number>
SIDT/LIDT –Store/Load IDTR
STI/CLI – Set/Clear Interrupt Flag(IF)
STR/LTR – Load/Store Task Register (TR)
INT n – Software Interrupt, invoke handler n
UD2 – Undefined Instruction Interrupt
INTO – Overflow Interrupt
0xCC form of INT 3 – Breakpoint Interrupt
IRET – Return from interrupt
Notes: <number>