## Slide 1: Intermediate x86 Part 4
Xeno Kovah – 2010
xkovah at gmail
Notes: <number>

## Slide 2: All materials are licensed under a Creative Commons “Share Alike” license.
http://creativecommons.org/licenses/by-sa/3.0/
<number>

## Slide 3: Interrupts & Debugging
<number>
We know that IDT[3] is the Breakpoint Exception, and that it’s important enough for INT 3 to have a separate one byte opcode form (0xCC).
INT 3 is what debuggers are using when they say they are setting a “software breakpoint” (the default breakpoint in most cases)
When a debugger uses a software breakpoint, what it does is overwrite the first byte of the instruction at the specified address. It keeps its own list of which bytes it overwrote and where. Then when breakpoint exception is received, it looks up the location, replaces the original byte and lets the instruction execute normally. Then typically it overwrites the first byte again (subject to configuration) so that the breakpoint will be hit if the address is executed again.
Notes: <number>

## Slide 4: Lab: ProofPudding.c
A program which reads its own memory in order to confirm that when a breakpoint is set, it overwrites a byte with the 0xCC form of the breakpoint interrupt, INT 3
<number>

## Slide 5: Hardware Support for Debugging
<number>
Most debuggers also have support for something called a “hardware breakpoint”, and these breakpoints are more flexible than software breakpoints in that they can be set to trigger when memory is read or written, not just when it’s executed. However only 4 hardware breakpoints can be set.
There are 8 debug registers DR0-DR7
  DR0-3 = breakpoint linear address registers
  DR4-5 = reserved (unused)
  DR6 = Debug Status Register
  DR7 = Debug Control Register
Accessing the registers requires CPL == 0
  MOV DR, r32
  MOV r32, DR
Vol. 3b, Sect. 18
Notes: <number>

## Slide 6: Picture This
<number>

## Slide 7: DR7 - Debug Control Register
<number>
L0-3 (local breakpoint enable) flags - Enables the DR0-3 breakpoint. But these flags are cleared on task switches to ensure that they do not fire when dealing with a different task.
G0-3 (global breakpoint enable) flags - Enables the DR0-3 breakpoint. Does not get cleared on task switch, which is what makes it global obviously.
LE & GE (local and global exact breakpoint enable) flags - If set to 1, enables detection of the exact instruction that caused a data breakpoint. Not supported on P6 microarchitecture and later, but if you need maximum compatibility for exact breakpoint detection you’re recommended to set both to 1.

## Slide 8: DR7 - Debug Control Register (2)
<number>
GD (General Detect) flag - If set to 1, causes a debug exception prior to MOV instructions which access the debug registers. The flag is cleared when the actual exception occurs though, so that the handler can access the debug register as needed.
The R/W0-3 are interpreted as follows:
  00 = Break on instruction execution only.
  01 = Break on data writes only.
  If(CR4.DE == 1) then 10 = Break on I/O reads or writes.
  If(CR4.DE == 0) then 10 = Undefined.
  11 = Break on data reads or writes but not instruction fetches.

## Slide 9: DR7 - Debug Control Register (3)
<number>
LEN0-4 bits specify what size the address stored in the DR0-3 registers should be treated as.
  00 = 1-byte
  01 = 2-bytes
  10 = Undefined (or 8 bytes, see note below)
  11 = 4-bytes.
While you might set a 1 byte size for an address pointing at the first byte of an instruction, on a break-on-execute, you might want to set a 4 byte breakpoint on writes to a memory location you know to be a DWORD.
“For Pentium 4 and Intel Xeon processors with a CPUID signature corresponding to family 15 (model 3, 4, and 6), break point conditions permit specifying 8-byte length on data read/write with an of encoding 10B in the LENx field.”

## Slide 10: DR6 - Debug Status Register
<number>
B0-B3 (breakpoint condition detected) flags - When the B{0,1,2,3} bit is set, it means that the {0th,1st,2nd,3rd} condition specified in DR7 has been satisfied. The bits are set even if the DR7 says that condition is currently disabled. I.e. software needs to crosscheck these bits against whether it currently cares.
BD (debug register access detected) flag - Indicates that the next instruction will try to access the debug registers. This flag only enabled if GD (general detect) flag in DR7 is set. Thus this signals if someone else was trying to access the debug registers. NO! MINE!

## Slide 11: DR6 - Debug Status Register (2)
<number>
BS (single step) flag - If set, the debug exception was triggered by single-step execution mode (talked about later).
BT (task switch) flag - Related to TSS so we don’t care
“Certain debug exceptions may clear bits 0-3. The remaining contents of the DR6 register are never cleared by the processor. To avoid confusion in identifying debug exceptions, debug handlers should clear the register before returning to the interrupted task.” Seems like an important point if you’re making a debugger :)

## Slide 12: So what actually happens when a hardware breakpoint fires?
<number>
It fires IDT[1], a Debug Exception
When it is an execute breakpoint or general detect (someone trying to access debug regs) it’s a fault.
For other cases It’s A Trap!
  That means if it was a break on write, the data is overwritten before the exception is generated. A handler which wants to show the before and after is responsible for keeping a copy of the before value.
Instruction breakpoints are actually detected before the instruction executes. Therefore if the handler doesn’t remove the breakpoint, and it just returned, the same exception would be raised over and over.
This is where the Resume Flag (RF) comes into play
Notes: <number>
Image from http://sydlexia.com/blogstuff/ackbar_its_a_trap.jpg

## Slide 13: Resume Flag (RF in EFLAGS)
<number>
When the RF is set, the processor ignores instruction breakpoints.
To set the flag, a debug interrupt handler would manipulate the EFLAGS stored on the stack and then use IRETD (POPF, POPFD, and IRET do not transfer RF from the stack into EFLAGS)
“The processor then ignores instruction breakpoints for the duration of the next instruction.” “The processor then automatically clears this flag after the instruction returned to has been successfully executed.”
Notes: <number>
Bullet 3 is quotes from 2008 manuals Vol 3a and 3b, sections 18.3.1.1 and 2.3 respectivly

## Slide 14: Trap Flag (TF in EFLAGS)
<number>
Only being able to invoke the debug exception handler on 4 addresses is somewhat limiting.
When TF is 1, it causes a debug exception after every instruction. This is called “single-step” mode.
  Useful for capabilities such as “step out” which just steps until it steps through a RET
Remember that we said that if the debug exception is in response to single stepping, it sets the BS flag in DR6.
The processor clears the TF flag before calling the exception handler, so if it wants to keep single-stepping it needs to set it again before returning.
Also, the INT and INTO instructions clear TF. So a single stepping debugger handler should compensate accordingly.

## Slide 15: WinDbg Hardware Breakpoints
Hardware Breakpoint = ba rather than bp. Stands for break on access, where access can be read/write/execute or port IO. Below is a simplified form of the command (see help page for full form)
ba Access Size Address
  Access
    r = read/write
    w = write
    e = execute
    i = I/O port (talked about later)
  Size. Width of data over which you want the breakpoint to have effect. Must be 1 for access = e, but can be 1, 2, 4, or 8 for other types
  Address. Where you want the breakpoint to be targeted.
<number>

## Slide 16: HW Breakpoint Examples
ba e 1 0x80541ac0
  Break on execute of address 0x80541ac0 (windbg specifies size must be 1 on break on execute)
ba w 4 0x80541ac0
  Break if anyone reads from the 4 bytes specified by 0x80541ac0 to 0x80541ac4
ba r 2 0x80541ac0
  Break if anyone reads or writes from byte 0x80541ac0 or 0x80541ac1(remember, the debug registers don’t have a way to specify only read)
<number>

## Slide 17: Lab: Watching the debugger debug
<number>
TryToRunTryToHide.c take 2
A discourse on the efficacy of using a hardware breakpoint on the INT 3 handler, rather than a software breakpoint ;)

## Slide 18: Malware Use of Debug Regs
<number>
“A packer such as tElock makes use of the debug registers to prevent reverse-engineers from using them. “
  http://www.securityfocus.com/infocus/1893
The Art of Unpacking (lists various anti-debug tricks including reading the debug registers)
  https://www.blackhat.com/presentations/bh-usa-07/Yason/Whitepaper/bh-usa-07-yason-WP.pdf
But I thought you had to be running in ring 0 to manipulate debug registers? Well, yes, but windows saves thread information (including the contents of the debug register) into a CONTEXT structure, and provides userspace a way to get and set thread context, thus letting malware detect .

## Slide 19: The New Stuff (Which I don’t yet know enough about to teach. Read 3b, Sect. 18.4 on your own)
<number>
“P6 family processors introduced the ability to set breakpoints on taken branches, interrupts, and exceptions, and to single-step from one branch to the next. This capability has been modified and extended in the Pentium 4, Intel Xeon, Pentium M, Intel CoreTM Solo, Intel CoreTM Duo, Intel CoreTM2 Duo, Intel CoreTM i7 and Intel AtomTM processors to allow logging of branch trace messages in a branch trace store (BTS) buffer in memory.”
The branch trace is basically a stack which holds pairs of addresses which represent the source of the branch and the destination.
Pedram Amini talked about the performance improvement vs. single step mode here:
  http://www.openrce.org/blog/view/535/Branch_Tracing_with_Intel_MSR_Registers

## Slide 20: Port I/O
<number>
“In addition to transferring data to and from external memory, IA-32 processors can also transfer data to and from input/output ports (I/O ports).”
“I/O ports are created in system hardware by circuity that decodes the control, data, and address pins on the processor. These I/O ports are then configured to communicate with peripheral devices.”
“An I/O port can be an input port, an output port, or a bidirectional port.”
Vol 1, Sect 13

## Slide 21: Ports
<number>
There are 2^16 8bit IO ports, numbered 0-0xFFFF.
Can combine 2 or 4 consecutive ports to achieve a 16 or 32 bit port.
“32-bit ports should be aligned to addresses that are multiples of four (0, 4, 8, ...).”

## Slide 22: Accessing the Ports
<number>
You cannot use the IN/OUT instructions to access the ports unless you have sufficient privileges.
There is a 2 bit IOPL (I/O Privilege Level) field in EFLAGS. You can only perform IO if CPL <= IOPL.
Also FYI, the STI/CLI instructions we saw before also are only allowed if CPL <= IOPL.
Most OSes set IOPL to 0
But think back to privilege rings. An appropriately modified OS (say, a paravirtualized one), could allow IOPL to be something like 2.
Notes: <number>
IOPL is one of those fields of EFLAGS which won’t change with a POPF unless you’re in ring0

## Slide 23: IN - Input from Port
<number>
Note it’s DX, not DL. That means the DX form can specify all 2^16 ports, but the IMM8 form can only specify 2^8 ports.
“When accessing a 16- and 32-bit I/O port, the operand-size attribute determines the port size.” (Because as usual there’s an overloaded opcode for 16/32 bit form)
  Remember if you’re in a 16 bit segment it’s 16 bit, if you’re in a 32 bit segment it’s 32 bit. But you can override it with an operand size instruction prefix which is talked about later.

## Slide 24: OUT - Output to Port
<number>
Basically the same caveat as IN

## Slide 25: Lab: ParlorTrick.c
Accessing the vmware “backdoor” IO port.
For more tricks, see VMBack - http://chitchat.at.infoseek.co.jp/vmware/backdoor.html
<number>

## Slide 26: The 8042 keyboard controller
Lots of good info here: http://www.computer-engineering.org/ps2keyboard/
The original IBM PC used a chip by the name of 8042 as the keyboard controller. PS/2 keyboards use this chip, and luckily for us, so do VMWare virtual machines by default (since PS/2 is way simpler than USB)
The 8042 has a status/command register mapped to IO port 0x60 and a data register mapped to IO port 0x64
<number>

## Slide 27: Lab: basic_hardware.c Spooky action at a distance
Code taken as-is from http://www.rootkit.com/vault/hoglund/basic_hardware.zip
Starts a timer in the kernel which calls a function every 300ms. That function talks to the keyboard controller using port IO, and sets a new value for the LED indicator lights for Num/Caps/Scroll lock
<number>

## Slide 28: Lab: bhwin_keysniff.c Low level keystroke logging
Code taken from http://www.rootkit.com/vault/hoglund/basic_keystroke.zip with changes and hackery to get it to work as noted inline
Every time a key is pressed/released, it triggers an interrupt. In our case it is INT[0x93] which is usually handled by i8042prt.sys’s I8042KeyboardInterruptService() function.
Keys are represented as “scancodes” indicating position on the keyboard, not ASCII values.
This code hooks the keyboard interrupt( i.e. puts itself into the IDT descriptor) and then reads and stores the incoming scancode, puts it back into the buffer, and then calls the original handler.
<number>

## Slide 29: HW Breakpoint Examples
WinDbg commands to set a breakpoint on port IO
ba i 1 0x60
  Break on 1 byte access to port address 0x60
  The value read in will be in al
ba i 4 0x60
  Break on 1-4 byte access to port address 0x60
  The value read in will be in al, ax, or eax depending on the size used in the IN instruction
<number>

## Slide 30: Debug Reg Keyboard Sniffer
We just saw from the bhwin_keysniff.c source, that you speak to port 0x60 to talk to the 8042 keyboard controller.
We saw earlier that the debug registers have an option to break on port IO access.
Combine, and you get a keyboard sniffer which hooks the debug breakpoint handler rather than keyboard handler (but still has to hook the IDT to catch the debug register interrupts, INT 1).
It is admittedly fragile. If someone overwrites the debug reg entry, purposely or accidentally, it is blinded. But it could keep polling to check if it has been removed, and replace itself. Though sooner or later an analyst is going to wonder why his hardware breakpoints keep getting missed and overwritten.
PoC: http://www.rootkit.com/vault/chpie/0x60_hook.zip
<number>

## Slide 31: Tap Into Your Hidden Potential and Disassemble Binary Using Only THE POWER OF YOUR MIND!!!
Foretell the future (values of registers)!
Impress friends and cow orkers!
Be the life of the party!
Burn excess calories!
Live in infamy!
Call Now! Just 9 easy payments of 9.99!
<number>
Notes: Highly disappointed that I couldn’t get the psychic lady picture as transparent in the background :(
<number>

## Slide 32: (Dramatic) Intel Instruction Format
<number>
“r/m32”

## Slide 33: Explaination of “r/m32s”
<number>
What I called an “r/m32” is actually the combination of the “ModR/M” and “SIB” bytes from the previous slide
I had previously promised to get into why AND has a /4 in its opcode column.
Vol. 2a page 3-2 section 3.1.1.1’s explanation of the opcode column says:
“/digit - A digit between 0 and 7 indicates that the ModR/M byte of the instruction uses only the r/m (register or memory) operand. The reg field contains the digit that provides an extension to the instruction's opcode.”
“/r — Indicates that the ModR/M byte of the instruction contains a register”
operand and an r/m operand.
And here’s what 3.1.1.2 says about the instruction column:
OK, what’s a “ModR/M” byte?

## Slide 34
<number>
The src/dst register
part
The memory part

## Slide 35
<number>
This is misleading. Looking at the chart you would think you can’t access [ESP], but you can (if your instruction either uses /r (or /5? Any such instruction?)
The base register

## Slide 36: Examples of testing
<number>
(You have to put each _emit on its own line, I just wrote them this way for conciseness)
__asm{_emit 0x80; _emit 0x20; _emit 0xFF;};
80 20 FF and byte ptr [eax],0FFh
__asm{_emit 0x80; _emit 0x60; _emit 0x20; _emit 0xFF;};
80 60 20 FF and byte ptr [eax+20h],0FFh
__asm{_emit 0x80; _emit 0x00; _emit 0xFF;};
80 00 FF add byte ptr [eax],0FFh
Wait, add? But I’m still using 0x80 at the front?!

## Slide 37: Overloaded Opcodes
We’ve already seen cases where opcodes are overloaded for different data size, but some like 0x80 are also overloaded for things like arithmetic/logical operations
Back to the tables!
<number>

## Slide 38: More than one way to skin an instruction
If you read “skin” to mean “remove the skin of” rather than “put a skin onto”, then you are sick and should seek help :P
ModRM = 0x0 = [EAX]
ModRM = 0x8 = [EAX] - To the tables!
Note that you only have the option of using either if your opcode is specified with a /r (like MOV) rather than a /digit (like AND/ADD)
ModRM = 0x4 = Add SIB, SIB = 0x0 = [EAX] therefore 0x4 0x0 = [EAX]
Yet another reason trying to use binary signatures sucks in x86
<number>
Notes: And if you read “skin” in “put a skin onto” as a fleshy skin rather than
<number>

## Slide 39: Instruction Prefixes
There are 4 groups of prefixes specified
  Group 1: LOCK/REP/REPNE
  Group 2: Segment Override, Branch Hints (Seemingly unrelated, but put together because the prefix bytes are overloaded)
  Group 3: Operand-size override
  Group 4: Address-size override
<number>
Vol 2a, Sect 2.1.1

## Slide 40: Lock prefix
<number>
Lock prefix = 0xF0
Locks the memory bus, preventing anyone else from changing memory until the instruction is done
lock xchg eax, [ebx]
Used for creating the simplest mutual exclusion primitive – mutex
Cannot be applied to all instructions (see the specific instruction’s details)

## Slide 41: REP prefixes
<number>
REP/REPE/REPZ = 0xF3
REPNE/REPNZ = 0xF2
Both apply only to string (movs, stos, etc-ending-in-s) and in/out instructions
REP
0xA5 = movsd es:[edi], ds:[esi]
  0xF3 0xA5 = rep movsd es:[edi], ds:[esi]

## Slide 42: Segment Override Prefixes
<number>
“0x2E—CS segment override (use with any branch instruction is reserved)
0x36—SS segment override prefix (use with any branch instruction is reserved)
0x3E—DS segment override prefix (use with any branch instruction is reserved)
0x26—ES segment override prefix (use with any branch instruction is reserved)
0x64—FS segment override prefix (use with any branch instruction is reserved)
0x65—GS segment override prefix (use with any branch instruction is reserved)”
Note, they’re only reserved with conditional branches
FF 24 24 jmp dword ptr [esp]
65 FF 24 24 jmp dword ptr gs:[esp]
8B 04 24 mov eax,dword ptr [esp]
26 8B 04 24 mov eax,dword ptr es:[esp]

## Slide 43: Branch Hints
Tell the processor’s branch prediction unit to assume that a branch will be taken one way or the other.
Implicitly you would only do this when you knew that your code was structured such that it ran contrary to the default rules for branch prediction.
Since good compilers try to generate code with the branch prediction defaults in mind, one would only expect to see this with handcoded asm.
0x2E – Branch not taken
0x3E – Branch taken
These can only be used with conditional jumps (Jcc)
Note that they are also valid segment override prefixes (and since there are more segment override prefixes than 0x2E/0x3E, I’m not sure why it says the other things should not be used with branch instructions)
<number>

## Slide 44: Operand and Address Size Override Prefixes
<number>
0x66 – Operand Size Override
0x67 – Address Size Override
In both cases, if something was in a 32 bit segment, it would be using 32 bit size, but adding these before instructions forces operands or addresses to be treated as 16 bits. (And if things were in 16 bit segments these prefixes would force things to 32 bits)

## Slide 45: Lab: InstructionPrefixes.c
More looking at and playing with the various prefixes
<number>

## Slide 46: Madness no more!
<number>
This isn’t so bad!!!
That’s what you learned! :D

## Slide 47: The Big Picture
<number>

## Slide 48: Virtual Memory in Four Fruity Flavors
<number>

## Slide 49: Friends we’ve met along the way
<number>
CPUID – Identify CPU features
PUSHFD/POPFD – Push/Pop EFLAGS
SGDT/LGDT – Store/Load GDTR
SLDT/LLDT – Store/Load LDTR
RDTSC – Read TimeStamp Counter
MOV CR, r32 – (CR = Control Register)
MOV r32, CR – (CR = Control Register)
INVLPG – Invalidate page entry in TLB
SIDT/LIDT – Load/Store IDTR
STI/CLI – Set/Clear Interrupt Flag(IF)

## Slide 50: More Friendly Friends!
STR/LTR – Load/Store Task Register (TR)
UD2 – Undefined Instruction Interrupt
INTO – Overflow Interrupt
INT n – Software Interrupt, invoke handler n
0xCC form of INT 3 – Breakpoint Interrupt
IRET – Return from interrupt
MOV DB, r32 (DB = Debug Register)
MOV r32, DB (DB = Debug Register)
IN/OUT – Input/Output Port IO
LOCK prefix (if we had time for prefixes)
<number>

## Slide 51: Closing thoughts…
<number>
I tried to present most things in their Intel, mostly-OS-agnostic form, just using Windows as the example system due to robustness of the tools (and cause I’ve been forced to use it lately.)
You’re now more qualified to start digging into how any OS running on the x86 platform works. Just look for the relevant “* Internals” book, pdfs, presentations, etc.
You’re actually quite well suited to start exploring other architectures as well, having been exposed to the deep internals of x86 you can see the similarities and differences in other architectures and reason about where a given component is more or less trying to achieve the same functionality as what you already know, etc.

## Slide 52: Closing thoughts…
<number>
You’re also more qualified to start digging into how virtualization works
OS is to Process as Hypervisor is to ?
OS plays games among processes to share CPU time and memory. Hypervisor plays games among OSes to share CPU time and memory (and limited number of system control registers and structures).
Ask yourself the question “If I wanted to trick multiple OSes into thinking they were accessing the hardware as normal, when in fact only I do, what would I do with control registers? IO? Page tables?” Then you start to see why virtualization is eminently detectable on x86.
Then when you think about it in terms of tricking the OS, think about it in terms of maliciously tricking the OS, and you’ve got yourself a hypervisor-based rootkit :)

## Slide 53: Closing thoughts…
<number>
There are tool-users and tool-builders/understanders. When you learn reverse engineering by necessity, you are a tool user. When you look at the tool builders or the rock stars of RE, they are the understanders.
You now understand a lot more about how things work than many reverse engineers. (Note to self, see note)
“How does a debugger work” is a great interview question to ask to and drill down on with someone with lots of experience reverse engineering, to help understand if they’re a user or an understander :)
Notes: Talk about how I consider the core components of excellence in RE being a power-user with their tools, refining their analytical thought, and always going deeper to understand as much or more about the system than their adversary.
<number>

## Slide 54: Closing thoughts…
In general, kernel-mode rootkit researchers come from a background of knowing a lot of the OS and architecture level details
Very difficult to combat adversaries which know more than you about the system you’re defending.
You’re all now more qualified to work on my research! :D Hidden agenda #427 revealed!
<number>

## Slide 55: To be continued?
Once you successfully digest this material you will know nearly as much stuff about x86 as I do.
If there’s an Advanced x86 class, a big reason for it will be for me to nail down stuff I’ve been meaning to learn better…getting paid to share the knowledge with you would just be a side benefit :P
System Management Mode (hot topic in rootkits…you really want me to teach this, because if I do, I will try to pull together the existing SMM attacks into sweet sweet VM escape PoCs)
Hardware Virtualization (I’m less interested in virtualization at the vendor level and more interested in how it works)
Intel 64 bit (OS X >= 10.6 now native 64 bit)
Advanced Programmable Interrupt Controller (APIC) – Even deeper into how interrupts work. Useful for sending inter-processor interrupts on multi-CPU/core systems
Intel SpeedStep – manually controlling CPU throttling. A MS guy on a Windows developer list said if you’re not the OS you shouldn’t be messing with it, which just makes me want to do it more ;)
BIOS maybe, but probably not
<number>

## Slide 56: Other stuff
The Life of Binaries class
RE class(es?)
Vulnerabilities & Exploits class
Understanding Malware: Rootkits class?
Understanding Malware: Botnets class?
Advocacy!
Fill out the feedback!
<number>
Notes: <number>