## Slide 1: Intermediate Intel x86: Assembly, Architecture, Applications, and Alliteration
Xeno Kovah – 2010
xkovah at gmail
Notes: <number>
Approved for Public Release: 10-3349. Distribution Unlimited

## Slide 2: All materials are licensed under a Creative Commons “Share Alike” license.
http://creativecommons.org/licenses/by-sa/3.0/
<number>

## Slide 3: Credits Page
Your name here! Just tell me something I didn’t know which I incorporate into the slides!
Veronica Kovah for reviewing slides and suggesting examples & questions to answer
Murad Kahn for Google NaCl stuff
<number>

## Slide 4: Answer me these questions three
<number>
What, is your name?
What, is your quest?
What…is your department?
Notes: <number>
10 min

## Slide 5: Agenda
<number>
Part 1 - Segmentation
Part 2 - Paging
Part 3 - Interrupts
Part 4 – Debugging, I/O, Misc fun on a bun
Notes: <number>
2 min

## Slide 6: Miss Alaineous
<number>
Questions: Ask ‘em if you got ‘em
  If you fall behind and get lost and try to tough it out until you understand, it’s more likely that you will stay lost, so ask questions ASAP.
Browsing the web and/or checking email during class is a great way to get lost ;)
2 hours, 10 min break, 2 hours, 1 hour lunch, 1 hour at a time with 5 minute breaks after lunch
Adjusted depending on whether I’m running fast or slow (or whether people are napping after lunch :P)
Notes: <number>

## Slide 7: Class Scope
<number>
We’re going to only be talking about 32bit architecture (also called IA-32). No 16bit or 64bit.
Also not really going to deal with floating point assembly or registers since you don’t run into them much unless you’re analyzing math/3d code.
This class focuses on diving deeper into architectural features
Some new instructions will be covered, but mostly in support of understanding the architectural topics, only two are learning new instruction’s sake. As shown in last class, we have already covered the majority of instructions one will see when examining most programs.
Notes: <number>
2 min

## Slide 8: What I hope you get out of the class
<number>
A better understanding of Intel architecture and how it’s leveraged by OSes
  Which can in turn translate to understanding how OSes are virtualized
Knowledge of where hardware support for security exists, and how it is or isn’t used.
A base for understanding even more advanced features. The curiosity to independently explore advanced features.
The satisfaction that comes with knowing how something works at a very fundamental level.
Notes: <number>
You don’t know it now, but there are doors of understanding which are closed to you, until you’ve gone through other doors. I hope to open up some pathways to knowledge you didn’t know existed.

## Slide 9: Instructions Quiz
<number>
Learned around 26 instructions and variations
About half are just math or logic operations
NOP
PUSH/POP
CALL/RET
MOV/LEA
ADD/SUB
JMP/Jcc
CMP/TEST
AND/OR/XOR/NOT
SHR/SHL/SAR/SAL
IMUL/DIV
REP STOS, REP MOVS
LEAVE
Notes: <number>

## Slide 10: Stack Quiz: Example1.c
<number>
//Example1 - using the stack
//to call subroutines
//New instructions:
//push, pop, call, ret, mov
int sub(){
return 0xbeef;
}
int main(){
sub();
return 0xf00d;
}
sub:
00401000 push ebp
00401001 mov ebp,esp
00401003 mov eax,0BEEFh
00401008 pop ebp
00401009 ret
main:
00401010 push ebp
00401011 mov ebp,esp
00401013 call sub (401000h)
00401018 mov eax,0F00Dh
0040101D pop ebp
0040101E ret
Notes: <number>
I start this out by putting the “Saved EIP to return to function-who-called-main” and then they have to put the rest.

## Slide 11: Madness
<number>
That’s what you’re going to learn! :D
Notes: <number>

## Slide 12
<number>
THIS!
IS!
INTERMEDIATE
X86!!!
As a nerd I actually find this graphic to be disappointingly inaccurate because this is not where he said the line…I couldn’t find a good picture of that moment.
If I took any pride in my work I would have rented the video and taken a screen shot…
ME
You
by the
end
Notes: <number>

## Slide 13: Morning Warm Up CPUID - CPU (feature) Identification
<number>
Different processors support different features
CPUID is how we know if the chip we’re running on supports newer features, such as hardware virtualization, 64 bit mode, HyperThreading, thermal monitors, etc.
CPUID doesn’t have operands. Rather it “takes input” as value preloaded into eax (and possibly ecx). After it finished the outputs are stored to eax, ebx, ecx, and edx.
Notes: <number>
You’re big kids now, I let you see real manual definitions :P

## Slide 14: How do we even know if we can use CPUID?
<number>
CPUID not added until late model 486s
ID Flag in EFLAGS (bit 21)
“The ability of a program or procedure to set or clear this flag indicates support for the CPUID instruction.” (Vol. 3a, Sect. 2.3)
How do we read/write to EFLAGS?
PUSHFD/POPFD
Notes: <number>

## Slide 15: PUSHFD - Push EFLAGS onto Stack
<number>
If you need to read the entire EFLAGS register, make sure you use PUSHFD, not just PUSHF. (I found Visual Studio forces the 16 bit form if you don’t have the D!)
Notes: <number>

## Slide 16: POPFD - Pop Stack Into EFLAGS
<number>
There are some flags which will not be transferred from the stack to EFLAGS unless you’re in ring 0.
If you need to set the entire EFLAGS register, make sure you use POPFD, not just POPF. (I found Visual Studio forces the 16 bit form if you don’t have the D!)
Notes: <number>

## Slide 17: Some Example CPUID Inputs and Outputs
<number>
REGISTER
BEFORE CPUID
EXECUTES
REGISTERS
AFTER CPUID
EXECUTES

## Slide 18: Lab: CPUID.c
<number>
int main(){
unsigned int maxBasicCPUID;
char vendorString[13];
char * vendorStringPtr = (char *)vendorString; //Move the address into its own register
//because it makes the asm syntax easier
//First we will check whether we can even use CPUID
//Such a check is actually more complicated than it seems (OMITED FROM SLIDES)
if(CheckIfWeCanUseCPUID() == 1){
__asm{
mov edi, vendorStringPtr; //Get the base address of the char[] into a register
mov eax, 0; //We're going to do CPUID with input of 0
cpuid; //As stated, the instruction doesn't have any operands
//Get back the results which are now stored in eax, ebx, ecx, edx
//and will have values as specified by the manual
mov maxBasicCPUID, eax;
mov [edi], ebx; //We order which register we put into which address
mov [edi+4], edx; //so that they all end up forming a human readable string
mov [edi+8], ecx;
}
vendorString[12] = 0;
printf("maxBasicCPUID = %#x, vendorString = %s\n", maxBasicCPUID, vendorString);
}
else{
printf("Utter failure\n");
}
return 0xb45eba11;
}
Notes: <number>

## Slide 19: CPUID Misc
<number>
I highly recommend Amit Singh’s CPUID info dumping program for *nix systems
  http://www.osxbook.com/blog/2009/03/02/retrieving-x86-processor-information/
Also see “Intel Processor Identification and the CPUID Instruction - Application Note 485” for a lot more info about CPUID
  http://www.intel.com/Assets/PDF/appnote/241618.pdf

## Slide 20: In the beginning, there was real mode. And it was teh suck.
<number>
Real-address Mode - (I call it Real Mode or maybe “For Reals Mode…Seriously. For Reals. Mode.”) “This mode implements the programming environment of the Intel 8086 processor with extensions (such as the ability to switch to protected or system management mode). The processor is placed in real-address mode following power-up or a reset.”
DOS runs in Real Mode.
No virtual memory, no privilege rings, 16 bit mode
Vol. 1, Sect. 3.1
Notes: <number>

## Slide 21: Processor Modes 2
<number>
Protected Mode - “This mode is the native state of the processor. Among the capabilities of protected mode is the ability to directly execute ‘Real-address mode’ 8086 software in a protected, multi-tasking environment. This feature is called virtual-8086 mode, although it is not actually a processor mode. Virtual-8086 mode is actually a protected mode attribute that can be enabled for any task.”
Virtual-8086 is just for backwards compatibility, and I point it out only to say that Intel says it’s not really its own mode.
Protected mode adds support for virtual memory and privilege rings.
Modern OSes operate in protected mode
Vol. 1, Sect. 3.1
Notes: <number>

## Slide 22: Processor Modes 3
<number>
System Management Mode - “This mode provides an operating system or executive with a transparent mechanism for implementing platform-specific functions such as power management and system security. The processor enters SMM when the external SMM interrupt pin (SMI#) is activated or an SMI is received from the advanced programmable interrupt controller (APIC).”
SMM has become a popular target for advanced rootkit discussions recently because access to SMM memory is locked so that neither ring 0 nor VMX hypervisors can access it. Thus if VMX is more privileged than ring 0 (“ring -1”), SMM is more privileged than VMX (“ring -2”) because a hypervisor can’t even read SMM memory.
Reserving discussion of VMX and SMM for Advanced x86 class
Vol. 1, Sect. 3.1
Notes: <number>

## Slide 23
<number>
From http://support.amd.com/us/Processor_TechDocs/24593.pdf

## Slide 24: Privilege Rings
<number>
MULTICS was the first OS with support for hardware-enforced privilege rings
x86’s rings are also enforced by hardware
You often hear that normal programs execute in “ring 3” (userspace/usermode) and the privileged code executes in “ring 0” (kernelspace/kernelmode)
The lower the ring number, the more privileged the code is
In order to find the rings, we need to understand a capability called segmentation
Notes: <number>

## Slide 25: Rings on x86
<number>
Vol. 3a
Sect. 5.5
Notes: <number>

## Slide 26: Paravirtualized Xen (requires a modified Guest OS) (Newest Xen instead uses hw VMX to be more privileged than OS kernel)
<number>
http://www.valinux.co.jp/imgs/pict/shot/tech/techlib/eos/xen_ia64_memory/figure5.gif
Notes: <number>

## Slide 27: Segmentation
<number>
“Segmentation provides a mechanism for dividing the processor’s addressable memory space (called the linear address space) into smaller protected address spaces called segments.” (emphasis theirs)
Vol.3a, Sect. 3.1 & 3.2.3
Notes: <number>

## Slide 28: Segment Addressing
<number>
“To locate a byte in a particular segment, a logical address (also called a far pointer) must be provided. A logical address consists of a segment selector and an offset.”
“The physical address space is defined as the range of addresses that the processor can generate on its address bus”
  Normally the physical address space is based on how much RAM you have installed, up to a maximum of 2^32 (4GB). But there is a mechanism (physical address extentions - PAE) which we will talk about later which allows systems to access a space up to 2^36 (64GB).
  Basically a hack for people with more than 4GB of RAM but who aren’t using a 64 bit OS.
Linear address space is a flat 32 bit space
If paging (talked about later) is disabled, linear address space is mapped 1:1 to physical address space
Vol.3a, Sect. 3.1
Notes: <number>

## Slide 29: Segmentation Restated
<number>
Segmentation is not optional
Segmentation translates logical addresses to linear addresses automatically in hardware by using table lookups
Logical address (also called a far pointer) = 16 bit segment selector + 32 bit offset
If paging (which is talked about later) is disabled, linear addresses map directly to physical addresses
Notes: <number>

## Slide 30: Assume paging is disabled for now linear address == physical address
<number>
Vol.3a, Sect. 3.1
The wool over your eyes
The Big Picture
Notes: <number>

## Slide 31: Segment Selectors
<number>
A segment selector is a 16 bit value held in a segment register. It is used to select an index for a segment descriptor from one of two tables.
  GDT - Global Descriptor Table - for use system-wide
  LDT - Local Descriptor Table - intended to be a table per-process and switched when the kernel switches between process contexts
Note that the table index is actually 13 bits not 16, so the tables can each hold 2^13 = 8192 descriptors
2 bit “privilege level”?
Hmmm…getting warm
push that onto a
mental stack
Notes: <number>

## Slide 32: The Six Segment Registers (Harbingers of DOOOOOM!!!)
<number>
CS - Code Segment
SS - Stack Segment
  “Stack segments are data segments which must be read/write segments. Loading the SS register with a segment selector for a nonwritable data segment generates a general-protection exception (#GP)”
DS - Data Segment
ES/FS/GS - Extra (usually data) segment registers
The “hidden part” is like a cache so that segment descriptor info doesn’t have to be looked up each time.
Notes: <number>

## Slide 33: Implicit use of segment registers
<number>
When you’re accessing the stack, you’re implicitly using a logical address that is using the SS (stack segment) register as the segment selector. (I.e. “ESP” == “SS:ESP”)
When you’re modifying EIP (with jumps, calls, or rets) you’re implicitly using the CS (code segment) register as the segment selector. (“EIP” == “CS:EIP”)
Even if a disassembler doesn’t show it, the use of segment registers is built into some of your favorite instructions.
Notes: <number>

## Slide 34: Explicit use of segment registers
You can write assembly which explicitly specifies which segment register it wants to use. Just prefix the memory address with a segment register and a colon
“mov eax, [ebx]” vs “mov eax, fs:[ebx]”
The assembly just puts a prefix on the instruction to say “When this instruction is asking for memory, it’s actually asking for memory in this segment”. We will talk about segment prefixes along with other instruction prefixes at the end of the class if we have time.
In this way you’re actually specifying a full logical address/far pointer.
<number>

## Slide 35: Lab: UserspaceSegmentRegisters.c
Userspace version of code which reads the segment
Moves from segment registers to memory, but the manual considers that the same as the other types of moves (but it does describe the special constraints which exist when moving to/from segment registers)
<number>

## Slide 36: Lab: KernelspaceSegmentRegisters.c
Kernel version of the same code, implemented as a kernel driver.
This isn’t a class on windows drivers, so
  open the “Windows XP Checked Build Environment” link on your desktop, navigate to IntermediateX86Code\KernelspaceSegmentRegisters
  type “build –c”
  run the magic “load.bat”
We use Sysinternals’ DebugView to see the output of the kernel space DbgPrint() statements. (They would also show up if attached to a kernel debugger.)
<number>

## Slide 37
<number>
1
2
3

## Slide 38
<number>
1
2
4
6: results
3
5:Confirm
5:Confirm

## Slide 39: Results for our WinXP systems (subject to change on other versions, service pack levels, etc)
Segment Register | RPL | Table | Index
CS = 0x1b | 3 | GDT | 3
SS = 0x23 | 3 | GDT | 4
DS = 0x23 | 3 | GDT | 4
ES = 0x23 | 3 | GDT | 4
FS = 0x3B | 3 | GDT | 7
GS = 0 | Invalid | Invalid | Invalid
<number>
UserspaceSegmentRegisters.c
Segment Register | RPL | Table | Index
CS = 0x8 | 0 | GDT | 1
SS = 0x10 | 0 | GDT | 2
DS = 0x23 | 3 | GDT | 4
ES = 0x23 | 3 | GDT | 4
FS = 0x30 | 0 | GDT | 6
GS = 0 | Invalid | Invalid | Invalid
KernelspaceSegmentRegisters.c

## Slide 40: Inferences
Windows maintains different CS, SS, & FS segment selectors for userspace processes vs kernel ones
The RPL field seems to correlate with the ring for kernel or userspace
Windows doesn’t change DS or ES when moving between userspace and kernel (they were the exact same values)
Windows doesn’t use GS
<number>

## Slide 41: One more time
<number>
GDT or LDT
One of the segment registers
(SS/CS/DS/ES/FS/GS)
Address used in some
assembly instruction

## Slide 42: GDT & LDT
<number>
All entries in these tables are “Segment Descriptor” structures
Special registers point to the base of the tables & specify their size

## Slide 43: Global Descriptor Table Register (GDTR)
<number>
The upper 32 bits ("base address") of the register specify the linear address where the GDT is stored.
The lower 16 bits ("table limit") specify the size of the table in bytes.
Special instructions used to load a value into the register or store the value out to memory
  LGDT - Load 6 bytes from memory into GDTR
  SGDT - Store 6 bytes of GDTR to memory
From Vol 3a.
Figure 2-5
Notes: <number>

## Slide 44: Local Descriptor Table Register (LDTR)
<number>
Like the segment registers, the LDT has a visible part, the segment selector, and a hidden part, the cached segment info which specifies the size of the LDT.
  The selector’s Table Indicator (T) bit must be set to 0 to specify that it’s selecting from the GDT, not from itself ;)
Special instructions used to load a value into the register or store the value out to memory
  LLDT - Load 16 bit segment selector into LDTR
  SLDT - Store 16 bit segment selector of LDTR to memory
From Vol 3a.
Figure 2-5
Notes: <number>

## Slide 45: Segment Descriptors
<number>
“Each segment has a segment descriptor, which specifies the size of the segment, the access rights and privilege level for the, the segment type, and the location of the first byte of the segment in the linear address space (called the base address of the segment).”
Notes: <number>
Yeah, that’s not an annoying way to specify the base or anything

## Slide 46: Descriptor Description
<number>
Base (32 bits) - linear address where the segment starts
Limit (20 bits) - Size of segment (either in bytes or 4kb blocks). End address of segment = base + limit.
G (Granularity) flag - if 0, interpret limit as size in bytes. If 1, interpret as size in 4kb blocks.
D/B - Default operation size flag. 0 = 16 bit default, 1 = 32 bit default. This is what actually controls whether an overloaded opcode is interpreted as dealing with 16 or 32 bit register/memory sizes
DPL (Descriptor Privilege Level - 2 bits) - Hmm…another interesting field which can range from 0 to 3 “with 0 being the most privileged level”. Push that onto your mental stack with the RPL.
Notes: <number>

## Slide 47: Segmentation and Opcodes
<number>
We can now dig into the simplification I told you in the intro class time about operands being treated as 32 bits just because you’re in protected mode.
Instead the processor (using the D/B bit in segment descriptors) interprets instructions as referring to address and operand sizes which are the same as the type of code or data segment you’re currently using. So if CS points to a 32 bit segment it uses 32 bit forms, and if it points at a 16 bit segment 16 bit forms.
A normal OS like Win/Mac/Linux is going to be using 32 bit segments for all normal code.
But what I said was good enough for before insofar as real mode doesn’t have the ability to use 32 bit segments, and therefore being in protected mode is a prereq to using 32 bit instructions.
Notes: <number>

## Slide 48: Descriptor Description 2
<number>
L Flag - 64 bit segment - ignore
S (System) Flag - 0 for System segment. 1 for Code or Data segment.
Type (4 bits) - Whether a segment is code or data, what the permissions are, whether it’s been accessed, and some other stuff. See next slide
P (Present) Flag - 0 for not present. 1 for present. “If this flag is clear, the processor generates a segment-not-present exception (#NP) when a segment selector that points to the segment descriptor is loaded into a segment register.”
Notes: <number>

## Slide 49: Code And Data Segment Types
<number>
Notes: <number>

## Slide 50: System Segment Types
<number>
Notes: <number>

## Slide 51: Lab: WinDbg & the !descriptor plugin
<number>
Found a WinDbg plugin for printing out IDT/GDT/LDT entries here
  http://www.codeguru.com/cpp/w-p/system/devicedriverdevelopment/article.php/c8035/
Made modifications relevant for the class such as printing out segment types, dumping entire table
First we need to get cozy with WinDbg
Notes: <number>

## Slide 52: Configuring VMWare for kernel debugging (tested on VMWare Server 1.x (Windows & Linux), & ESX & vSphere) (for ESX/vSphere don’t put the \\.\pipe\ in front of names)
Debuggee
*Add virtual serial port
*Use named pipe
- Windows name: \\.\pipe\whatever
- Linux name: /tmp/whatever
* This end is a server
(VM Debugger) Other end is a virtual machine
(Host Debugger) Other end is an application
<number>
VM Debugger
*Add virtual serial port
*Use named pipe
- Windows name: \\.\pipe\whatever
- Linux name: /tmp/whatever
* This end is a client
* Other end is a virtual machine
Host Debugger (Windows only)
*In WinDbg on the host when you’ve selected kernel debug
*Under the COM tab
- Port: \\.\pipe\whatever
- Click the “pipe” checkbox
This slide is for if you want to test this with your own VMs

## Slide 53: Connecting Debugger
<number>

## Slide 54: Connecting Debugger 2
<number>
\\.\pipe\whatever

## Slide 55
<number>
Mouse over to see description of which type of window it opens up

## Slide 56
<number>

## Slide 57
<number>

## Slide 58
<number>

## Slide 59
<number>

## Slide 60: Getting kernel debug symbols
<number>
You can also download symbols for offline debugging, in which case you’d just put put the folder you installed them into.
Also if you’re working on your own code, you can specify the folder where you have the .pdb files.
Notes: So that I can copy and paste ;): SRV*C:\WINDOWS\Symbols*http://msdl.microsoft.com/download/symbols
<number>

## Slide 61
Stop debugging
Step into
Step over
Step out
If “Source mode on” is clicked, when you step, it will step one source line at a time (assuming you have source)
If “Source mode off” is clicked, when you step, it will step one asm instruction at a time
Restart debugging
Continue
Set breakpoint
wherever the
cursor is currently

## Slide 62: WinDbg breakpoints
bp <address> : Set breakpoint
  Address can be number or human readable input like “main” or “Example1:main”
  This will be a software (int 3) breakpoint
bl : Breakpoints list
bd <bp ID> : Breakpoint disable
  <bp ID> as given by first column of bl
be <bp ID> : Breakpoint enable
  <bp ID> as given by first column of bl
bc <bp ID> : Breakpoint clear (delete)
Notes: <number>

## Slide 63: WinDbg misc of note
WinDbg lists the upper 32 bits of the GDTR as “gdtr” but the lower 16 bits as “gdtl”
Load the plugin in windbg with ".load protmode"
type "!descriptor" to list the possible commands (also supports tab completion)
<number>

## Slide 64: Stop!
<number>
We’ve actually overshot what we need to know to discuss the protection rings. They are the interaction between the Requested Privilege Level (RPL), Descriptor Privilege Level (DPL), and introducing the Current Privilege Level (CPL)
“The CPL is defined as the protection level of the currently executing code segment.” (Sect 2.1.1)
Privilege rings are automatically enforced by the hardware on certain operations.
  E.g. if attempting to jump/call/return from one segment into a different segment, the hardware will check the DPL of the target segment and allow the access only if CPL <= DPL
  E.g. if attempting to use many privileged assembly instructions, the hardware will only allow it if CPL == 0
Kernel is responsible for setting up userspace in the first place and making sure that when it allows userspace programs to run, their CPL == 3.
Notes: <number>

## Slide 65: You wish
You may be saying, “Oh, well, if the CPL is just the lower two bits of CS, I’ll just go ahead and load a segment selector which is the same as the current one, but with those bits set to 0, and I will be ring 0!”
Intel says “Yeah right” - “The MOV instruction cannot be used to load the CS register. Attempting to do so results in an invalid opcode exception”
<number>

## Slide 66: Call Gates ("I'm down with Bill Gates, I call him Money for short. I phone him up at home, and I make him do my tech support!" - Weird Al, "It's All About the Pentiums")
<number>
Call gates are basically a way to transfer control from one segment to another segment (possibly at a different privilege ring, possible at a different size in terms of whether it's 16/32 bits.)
But the key point is you don't want people to be able to call to anywhere in the other segment, you want the interface to be controlled and well-understood. So calling to a call gate brings code to a specific place which the kernel has set up.
Notes: <number>

## Slide 67: Call Gates 2
The CALL, RET, and JMP x86 instructions have a special form for when they are doing inter-segment control flow transfer (normal call, ret, jmps are intra-segment for reasons which will become clear shortly.)
Each of them takes a single far pointer as an argument (though in ret's case, it's popping it off the stack).
A call gate expects as many parameters as specified by the "Param Count" field on the previous slide (max of 16 due to 4 bit field). Parameters are just pushed onto the stack right to left like a normal cdecl/stdcall calling convention.
Return value from the far call is returned in eax.
__asm{call fword ptr 0x08:0x12345678};
<number>

## Slide 68: Surprise! No one uses segmentation directly for memory protection! :D
<number>
On most systems, segmentation is not providing the primary RWX type permissions, they instead rely on paging protections.
Vol.3a, Sect. 3.2.1
Notes: <number>

## Slide 69: Why did we even bother learning it?
Because it subtly influences aspects of the system.
  We’ve already seen that it’s the basis for the notions of userspace/kernel separation (which includes the enforcement of limiting access to privileged instructions), but it also influences most of the topics we will be covering in this class
On 32 bit systems, the GDT is required, and at least flat segmentation must be set up.
  Segmentation support mostly removed in x86-64, but it’s so embedded in the architecture, and chip makers so prize backward compatibility. that it will continue to influence design for a while.
It’s just good to understand how stuff works as accurately as possible :)
<number>

## Slide 70: Who uses segmentation for memory protection?
<number>
Paravirtualized Xen uses it to protect the hypervisor from the OS. Jives with the notion of putting the OS in ring 2 per the picture we saw early on. (http://www.cs.uiuc.edu/class/sp06/cs523/lectures/05/523-5-xen.pdf)
Google Native Client (NaCl)!?
  Thanks to Murad Khan for pointing this out
  System for sandboxing browser plugins, which aims to allow the plugin to be custom compiled to x86 code, and then it only executes x86 instructions natively if they meet criteria which ensures NaCl can analyze them to ensure safety
  Segmentation is used to provide a “data sandbox” which the code cannot access outside of
  Combination of a lot of other academic work, but segmentation is basically just an optimization to prevent having to intercept reads/writes looking for things targeted to the outside of the sandbox (can just check at the analysis stage)
  http://nativeclient.googlecode.com/svn/data/docs_tarball/nacl/googleclient/native_client/documentation/nacl_paper.pdf
Notes: <number>

## Slide 71: Misc usage of segments
On Windows as a RE you will see access to the FS segment register frequently (e.g. mov eax, fs:[0]). Windows manages the FS register to have it always pointing at the base of the Thread Environment Block (TEB) which is used to store some per-thread information.
In the Intro x86 class I noticed in a Linux/GCC example which had stack cookies enabled, it seemed to be pulling the random cookie from some structure based at GS. But I don’t know what it was, so if anyone wants to figure that out and LMK, I’d be much obliged.
<number>

## Slide 72: Why isn’t segmentation widely used?
<number>
Answer: I dunno. Ideas? LMK
Speculation: It’s one of the standard security tradeoffs, security vs. performance. How much overhead does it add? Probably not much, but since many OS design decisions were made in the unfortunate time after COTS overtook MLS (Multi-level secure) OSes, the designers probably sided with performance.
Speculation 2: With only 6 segment registers, you can’t have a 1:1 mapping of segments to binary memory sections, because some binaries have > 6 sections, so then the questions becomes, what are the most appropriate places to apply segmentation (other than code vs data), how frequently do you want to switch, or what if there’s no compiler support?
Speculation 3: Wikipedia says segmentation “make[s] programming and compilers design difficult because the use of near and far pointers affect performance” Citation needed ;), but I can see how it would make compilers more difficult. How does the compiler know what your OS is doing with segmentation?
Speculation 4: All of the above. Whatever it is, support for segmentation was mostly removed in x86-64
Notes: <number>
Not this citation http://en.wikipedia.org/wiki/X86, that’s just where I got it from :P

## Slide 73: Misc: NoPill & ScoopyNG, using LDT/GDT to detect that we’re in a VM
<number>
NoPill
  http://www.offensivecomputing.net/files/active/0/vm.pdf
  Redpill equivalent which profiles the LDTR rather than IDTR (talked about later)
  Done because RedPill signature can have false positives outside of VMs.
ScoopyNG
  Does 7 checks including LDT/GDT as well as other things like the VMWare I/O channel
  http://www.trapkit.de/research/vmm/scoopyng/index.html
  Source code is in the zip file
Notes: <number>

## Slide 74: Misc Instructions Picked Up Along The Way
<number>
CPUID – Identify CPU features
PUSHFD/POPFD – Push/Pop EFLAGS
SGDT/LGDT – Store/Load GDTR
SLDT/LLDT – Store/Load LDTR
Notes: <number>
Canned Joke:
Ask CPUID like “What can you get from CPUID?”
Then when the person answers say “I would have also accepted ‘What CAN’T you get from CPUID!’” ;)