## Slide 1: Advanced x86: BIOS and System Management Mode Internals
John Butterworth & Xeno Kovah
Part 2

## Slide 2: All materials are licensed under a Creative Commons “Share Alike” license.
http://creativecommons.org/licenses/by-sa/3.0/
Attribution condition: You must indicate that derivative work
"Is derived from John Butterworth & Xeno Kovah’s ’Advanced Intel x86: BIOS and SMM’ class posted at http://opensecuritytraining.info/IntroBIOS.html”
Notes: Attribution condition: You must indicate that derivative work
"Is derived from Xeno Kovah's ’Introductory Intel x86: Assembly, Architecture, and Applications’ class"

## Slide 3: System Management Mode (SMM)
SMM: Ruling the hen house since
~1993*
* With Intel Management Engine present, does SMM still rule the hen house? We're not sure yet!

## Slide 4: System Management Mode (SMM) Overview
Most privileged x86 processor operating mode
Runs transparent to the operating system
When the processor enters SMM, all other running tasks are suspended
SMM can be invoked only by a System Management Interrupt (SMI) and exited only by the RSM (resume) instruction
Intended use is to provide an isolated operating environment for
  Power/Battery management
  Controlling system hardware
  Running proprietary OEM code
  etc. (anything that should run privileged and uninterrupted)

## Slide 5: System Management Mode (SMM) Overview
The code that executes in SMM (called the SMI handler) is instantiated from the BIOS flash
Protecting SMM is a matter of protecting both the active (running) SMRAM address space but also protecting the flash chip from which it is derived
  Protect itself (SMBASE (location), SMRAM Permissions)
  Write-Protect Flash
So far in our research, only about 5% of SMRAM configurations were directly unlocked and vulnerable to overwrite
However, since > 50% of the BIOS flash chips we've seen are vulnerable, that means > 50% of SMRAM will follow suit

## Slide 6
This figure shows how the processor moves in and out of SMM
  IA32e is Long Mode (64-bit mode)
SMM can be entered from any CPU operating mode
SMI# always causes the processor to enter SMM
RSM causes the processor to return the operating mode it was in prior to the SMI
The only way in and out of SMM is through an SMI# and a RSM, respectively
From Intel Vol. 1. Ch "System Management Mode"

## Slide 7: System Management Interrupt (SMI)
SMM can only be invoked by signaling a System Management Interrupt (SMI)
SMI’s can be received via the SMI# pin on the processor or through the APIC bus
SMI’s cannot be masked like normal interrupts
SMI’s are independent from the processor’s interrupt- and exception-handling mechanism and the local APIC
SMI’s take precedence over non-maskable and maskable interrupts
  Including debug exceptions and external interrupts
If an SMI and NMI occur at the same time, only the SMI will be handled

## Slide 8: SMI# vs. SMI
In the datasheets you will see references to SMI# and SMI
SMI# refers to the assertion of an external SMI
  SMI# is a pin on the processor
  Hardware devices can trigger this SMI# on various conditions (power, thermal, etc.)
  Software can also generate SMI# as a side-effect to writing to a register/device in such a way that it generates an SMI#
SMI refers to that which is software-generated and delivered via the APIC bus
  CPU/BIOS can trigger these
  And so can you with sufficient privileges
You can programmatically set some register combinations that trigger SMI#

## Slide 9: Causes of SMI#
Just an example, your ICH/PCH will list them for your system
Notes: SCI are interrupts for ACPI, not part of this class

## Slide 10: Generating SMI: APM
This is applicable to systems that support Advanced Power Management (most do these days)
Fixed I/O range, so it cannot be relocated
Check your I/O Controller Hub datasheet to verify its supported
Writes to 0xB3 do not trigger an SMI#, only the write to 0xB2
0xB3 can be used to pass information

## Slide 11: Advanced Power Management (APM)
APM_CNT (0xB2) is the control register
APM_STS (0xB3) is the status register
Located in I/O Address space
Registers are R/W
Note: APM != ACPI, but even on the Dell E6400 running Windows 7 which uses ACPI 2.0, this still triggers an SMI#
  The PCH datasheets (up to 8-series) also still list these under the fixed IO address
  Have not been able to test on a newer system
Notes: Check PCH and include location, if different, otherwise note its static location. Its in LPC so it should be the same

## Slide 12: APM_CNT & APM_STS
Writing a byte to port 0xB2 will trigger an SMI#
Writing to 0xB3 does NOT trigger the SMI#.
Can be used to pass information to the SMI handler.
Control flow through the SMI handler can be determined by the values in ports B2 – B3h
Usage: Could tell the SMI handler to measure Hypervisor memory, or initiate a BIOS update

## Slide 13: Examples
OUT 0xB2, 0x12
MOV DX, 0x1234
OUT 0xB2, DX
OUT 0xB3, 0x34
OUT 0xB2, 0x12
Generates SMI. SMI handler can read port 0xB2 to see that 0x12 was passed.
Writes 0x34 to 0xB3 and 0x12 to 0xB2 all in one shot (Generating SMI).
Writes 0x34 to 0xB3 and then writes 0x12 to 0xB2. SMI is triggered only on the write to 0xB2.

## Slide 14: Generating SMI via APIC
  We've not yet had time to play with this
  Should be able to generate SMI by programming the Interrupt Command Register in the APIC
  Architecture (and APIC type) dependent
  There is also a Self IPI register

## Slide 15: “Corollary” SMI# Generation
Looking through the datasheets there are various (too many to show) register bit-combinations that will also generate an SMI
For now I’m going to call this a corollary SMI#. Software is setting a register bit that incidentally generates an SMI#

## Slide 16: vulnBIOS specific: SMI Invocation Example
  Open a port IO window in RW-E at address 0xB2
  Type in the number 1 and hit enter
    I choose 1 because I know it to be a ‘safe’ value to enter
  Notice anything?
    (You’re not supposed to)
  The system just transitioned into SMM, executed code, and then exited SMM

## Slide 17: vulnBIOS specific: SMI Invocation Example
  Now open a memory window in RW-E to 0x90030
  And view it as a dword

## Slide 18: vulnBIOS specific: SMI Invocation Example
  Output 0x3333 to ports B2-B3h
  Notice the memory at 0x90030 is now changed
  This is a (very) contrived example but it’s difficult to “show” the effects of SMM
  We’ll see another more real-world example later during the BIOS flash portion of the course
  The point is, in SMM the processor can touch anything it’s able to without any interference
*This example is only applicable on an E6400 running the class’ customized BIOS

## Slide 19: SMI Communication Byte Patterns
  You can search for instances where a program is communicating with SMM via port IO by searching for byte patterns like those above
  To locate triggering of SMI via port 0xB2, you can search for the bytes “E6 B2” and “E7 B2” in IDA Pro
    Single byte searches for EE and EF yield many false-positives so analyze the code before it to ensure that the DX register contains B2
  APIC accesses will be trickier as they are memory-mapped
    I do not have any examples of this SMI at this time
From Intel Vol. 2

## Slide 20: SMI Byte Patterns Example
  Searching for instances of “E6 B2” and “E7 B2” in IDA will yield a list of examples like that on the left
  Most importantly, IDA provides an interesting clue here to a problem that we’ll be covering shortly…
  And is actually the only reason this slide is included

## Slide 21: SMI Invocation Counter
  So we’ve seen that there are a lot of events that can generate SMI and we’ve generated some on our own as well
  One logical question is: how frequently are these generated?
  As always, the answer is “it depends”
  On a system like a laptop, SMM will likely be called frequently to check the battery/power status
    Should be an SMI# in that case
  But on a desktop it may be called much less frequently
  Not that you can actually see it happening, since it’s transparent
  However, our lab system has been specially modified to provide you more insight to this so let’s take a look!

## Slide 22: vulnBIOS specific: SMI Invocation Counter
  On your E6400 lab machine, open a memory window to address 0x90000 using RW-E
  Viewing as a DWORD, look at offset 0x90000
  This value increments by one every time the system enters SMM
  This is not a standard feature!
  I added a custom SMI-handler to answer the question of how frequently a system can enter SMM
  Presumably because this is a laptop, SMM is entered about 1/second to check battery status/power
    Desktops may enter SMM far less frequently (like minutes apart)
  Notice that you don’t notice your system freezing

## Slide 23: SMI Counter (MSR)
  And as if answering my wishes for some way to track how frequently SMM is entered, I found this in Intel’s Software Programming Guide (Chapter 35, MSRs)
  It’s only available on Nehalem and later processor families (new stuff)
  Trying to read this will crash any system that doesn’t support it
    I hope you read this before trying ;)
Nehalem (Core i series & Xeon) and later architectures only!
From Intel Vol. 3. Ch. "Model Specific Registers (MSRs)"

## Slide 24: Periodic SMI#
  More as a side note (but related to the SMI counter), SMI# can be configured to fire periodically
  This way it can be guaranteed that SMI will be generated at least once every 8, 16, 32, or 64 seconds
  This register is R/W and resides on the LPC bus (D31:F0, offset A0h, bits 1:0)

## Slide 25: Entering SMM
When receiving an SMI, the processor waits for all instructions to complete and stores to complete
SMI interrupts are handled on an architecturally defined “interruptible” point in program execution
  Like an instruction boundary:
XOR EAX, EAX
ADD EAX, 1
Architecturally “interruptible” point
Processor saves the context in SMRAM and begins executing the SMI Handler
In a multi-core processor, no SMI handler code is executed until all cores have performed the above and entered SMM

## Slide 26: Entering SMM due to IO
IO Instruction restart field is located in the state save area in SMRAM
  SMBASE + 8000 + 7F00h
If an IO instruction to a device triggers an SMI, the SMI handler has the option of re-executing that instruction upon returning from SMM
  Example: If a device is asleep, port IO to it may generate SMI#. The SMI handler can then wake up the device and re-execute the instruction that generated the original SMI#
Similar to the auto HALT restart. The SMI handler can return execution either the instruction that generated the SMI# or to the instruction following it
From Intel Vol. 3. Ch. "System Management Mode"

## Slide 27: Exiting SMM: RSM
The only way to exit SMM is through the RSM instruction
  Or system shutdown
Returns control to the application program or operating-system procedure that was interrupted by the SMI
The processor’s state is restored from the save state area within SMRAM. If the processor detects invalid state information during state restoration, it enters the shutdown state.
The operating mode the processor was in at the time of the SMI is restored.
RSM can only be executed from within SMM
  So if you see this, you are debugging the SMRAM code
  RSM opcodes are: 0x0F 0xAA
  In our E6400, you can see SMRAM and the RSM instruction at DFF0_5AFDh
Executing RSM while not in SMRAM generates an invalid opcode exception
From Intel Vol. 2

## Slide 28: SMRAM
So we have talked about what causes the system to enter SMM
And we’ve (sort of) even “seen” it happen
  As best as possible
But we haven’t talked about SMM’s address space yet …

## Slide 29: SMRAM
SMRAM is the address space where the processor switches to upon entering SMM
This address space contains the SMI handler code and data
The processor’s pre-SMI context state save information is saved at a pre-defined location in SMRAM (offset from SMBASE)
SMBASE is the base address of SMRAM and can be located in either system memory or another location defined by the vendor (separate RAM)

## Slide 30: Address Space Layout
First off, lets define the terms SMBASE and SMRAM
SMRAM refers to the entire range (or ranges) where the SMI handler code and data is located
SMBASE is the address denoting the base address of SMRAM for a processor (or core)
  Each core will have its own SMBASE, typically staggered by the size of the state save area
The state save area(s) and entry point(s) are offset from SMBASE
SMBASE is defined in a field stored in the state save area within SMRAM
  Always at the same offset from SMBASE (FEF8h)
  A 32-bit value containing the physical address of SMRAM (SMBASE)
  Even in x64 architecture
Therefore SMRAM itself is re-locatable by changing the value of SMBASE
We’ll talk about where in physical memory SMBASE/SMRAM is likely to be located in a bit

## Slide 31
Default SMBASE on startup is 30000h, but can be relocated
SMI Handler Executable code entry point is always at SMBASE + 8000h
  CPU always begins executing at SMBASE + 8000h
Multi-core systems will (had better!) have their SMBASE offset by N bytes from each other. For example:
  Core 0 defines SMBASE as A_0000h, will enter SMI handler at A_8000h
  Core 1 defines SMBASE as A_1000h, will enter SMI handler at A_9000h
.
.
.
.
SMBASE
SMBASE + 8000h
SMI Handler (code) Entry Point
SMBASE + SMRAM Size
Start of State Save Area
SMBASE + 8000h + 7E00h (32 bit)
SMBASE + 8000h + 7C00h (64 bit)
SMBASE + 8000h + 7FFFh

## Slide 32
State save address starts at SMBASE + 8000h + 7FFFh
  SMBASE + FFFFh
For 32-bit CPU’s, the state-save area is 200h bytes
State save area extends down to SMBASE + 8000h + 7E00h
  SMBASE + FE00h
.
.
.
.
SMBASE
SMBASE + 8000h
SMI Handler (code) Entry Point
SMBASE + SMRAM Size
Start of State Save Area
SMBASE + 8000h + 7E00h (32 bit)
SMBASE + 8000h + 7C00h (64 bit)
SMBASE + 8000h + 7FFFh

## Slide 33
32-Bit
From Intel Vol. 3. Ch. "System Management Mode"

## Slide 34
State save address starts at SMBASE + 8000h + 7FFFh
  SMBASE + FFFFh
For 64-bit CPU’s, the state-save area is 400h bytes
The state-save extends down to SMBASE + 8000h + 7C00h
  SMBASE + FC00h
.
.
.
.
SMBASE
SMBASE + 8000h
SMI Handler (code) Entry Point
SMBASE + SMRAM Size
Start of State Save Area
SMBASE + 8000h + 7E00h (32 bit)
SMBASE + 8000h + 7C00h (64 bit)
SMBASE + 8000h + 7FFFh

## Slide 35
64-Bit
From Intel Vol. 3. Ch. "System Management Mode"

## Slide 36
SMBASE field for both 64-bit and 32-bit architectures is always located at the same offset from SMBASE (FEF8h)
64-Bit

## Slide 37
The remaining area is free for use as SMI handler code and data
Total size of SMRAM region is defined by the BIOS when it configures SMM
.
.
.
.
SMBASE
SMBASE + 8000h
SMI Handler Entry Point
SMBASE + SMRAM Size
Start of State Save Area
SMBASE + 8000h + 7E00h (32 bit)
SMBASE + 8000h + 7C00h (64 bit)
SMBASE + 8000h + 7FFFh

## Slide 38
Core 1 SMI Entry Point
Each core will have its own SMBASE address offset from the other core(s) SMBASE addresses
  Like 1000h bytes per the above 32-bit example
Technically, another core could define its SMBASE in a completely separate memory address
  In this diagram I show them sharing the same SMRAM memory range
  In practice, some cores will simply execute a dead loop
Core 0 SMBASE
Core 0 SMBASE + 8000h
Core 0 SMI Entry Point
Core 0 State Save Area
Core 0 SMBASE + FFFFh
Core 1 SMBASE
Core 1 SMBASE + FFFFh
Core 1 SMBASE + 8000h
Core 1 State Save Area
D000_0000h
D000_1000h
D000_0000h
D000_9000h
D000_FFFFh
D000_FE00h
D001_0FFFh
D001_0E00h

## Slide 39: SMRAM Location
Technically, SMRAM can be located anywhere in the 4GB memory address space
SMBASE can be overwritten by the SMI handler
Typically SMRAM is relocated at least once:
  On system startup, the first time the system enters SMM, SMBASE is at 0x30000
  SMI handler starts executing at 0x38000
  There is no reason it needs to stay at that address
Intel defines a few locations for SMRAM
  But it really is a flexible system and can be put anywhere
  I think these guidelines are provided to make configuration easier for the BIOS developers and to avoid areas where SMRAM may overlap with other regions
  This is all part of building that memory map

## Slide 40: Standard SMRAM Locations
On ICH/MCH chipsets there are 3 standard locations for SMRAM
On PCH chipsets the High Address (HSEG) is no longer supported (so 2 locations)
Technically the base address of SMRAM can be relocated by the SMI handler
  But there are reasons these guidelines should be followed and for all practical purposes SMRAM will be in TSEG

## Slide 41: Compatible SMRAM (Legacy Video Area)
Fixed address space
Legacy VGA space (A_0000 - B_FFFFh)
Confusingly called C Range or C-Seg for “Compatible”
  So I may incorrectly state it’s address to start at C_0000h
When compatible SMM space is enabled, SMM-mode processor accesses to this range are routed to physical system memory at this address.
Non-SMM-mode processor accesses to this range are considered to be to the video buffer area.
Legacy (DOS) Compatibility Range

## Slide 42: Enabling Compatible SMRAM
This address space is enabled by asserting the G_SMRAME bit
  I believe G_SMRARE is a typo in the datasheet
The register containing this bit (SMRAMC) will be located in a different place depending on the architecture
  On our E6400 it is located in the DRAM Controller (D0:F0) at offset 9Dh
  On a Haswell system, for example, it is also located in the DRAM controller but at offset 88h

## Slide 43: TSEG (Top of Main Memory Segment)
Variable address space
  In terms of size and location
Located at:
TOLUD – STOLEN – TSEG_SZ
to TOLUD – STOLEN
STOLEN refers to Graphics Memory Stolen, which is optional and can be zero
New architecture enables more customized location/size of TSEG
STOLEN
When extended SMRAM space is enabled, processor accesses to the TSEG range when the processor is not in SMM are treated as invalid
Non-processor originated accesses are not allowed to SMM space.

## Slide 44: Enabling TSEG
TSEG is enabled differently depending on the architecture
On MCH chipsets, it was defined in the ESMRAMC register
Either 1, 2, or 8MB in size for TSEG (defined in bits 2:1)
On our E6400 it’s in D0:F0, offset 9Eh
Newer systems offer more flexibility in TSEG size and location

## Slide 45: Enabling TSEG on new platforms
On newer systems the size of TSEG is more flexible in its programming
The offset of this register and its method of programming is dependent on the memory controller (which exists either in the MCH or the processor)
Notes: Note that on newer systems it gets its own lock bit, and is no longer dependent on D_LCK

## Slide 46: HSEG (High SMM Memory Space)
Fixed address space
FEDA_0000 to FEDB_FFFFh
When enabled (if supported), A_0000h to B_FFFFh are remapped to high memory
Not supported in PCH chipsets
Note: TSEG is located under TOLUD which is located at the bottom of this diagram

## Slide 47: Enabling HSEG
HSEG is enabled when bit 7 of the ESMRAMC bit is set
Not supported on PCH systems and later

## Slide 48: SMRAM Combinations (MCH-based)
Up to two memory locations can be used for SMRAM on a system
There is still only one SMBASE per core
Global Enable means that SMM compatible space is turned on
Note that enabling HSEG disables the Compatible C-range
Disabling the C-range disables all other ranges
So if you’re using TSEG, there is guaranteed to be either the C-range or the H-range also present

## Slide 49: SMRAM Combinations (PCH-based)
Up to two memory locations can be used for SMRAM on a system
  Which is good since on PCH there is only the Compatible and TSEG ranges; HSEG is no longer supported
As you can see, this means that the Compatible range is always enabled if TSEG is enabled
So the only question is whether or not you use TSEG

## Slide 50: Demo: Locating SMRAM
First let’s see what address ranges are enabled on our system for SMRAM
Open RW-Everything and select PCI devices, device 0, function 0 (the DRAM Controller)
Look at offset 9Dh (SMRAMC register)
See if bit 3 (G_SMRAME) bit is set
Compatible SMRAM at A_0000 to B_FFFFh is set

## Slide 51: Demo: Locating SMRAM
Let’s now check to see if TSEG (or HSEG) is enabled
We know we cannot be using both along side the compatible C range
Look at the register at offset 9Eh (ESMRAMC)
Notice that TSEG Enable bit 0 is asserted
  By default then, HSEG is not enabled, but we can also see that bit 7 is not asserted
TSEG Yes
HSEG No

## Slide 52: Lab: Find TSEG Base/Limit
So we know that Compatible SMRAM is enabled, and that is always at a fixed address A_0000 to B_FFFFh
But TSEG is dependent on other addresses
The TSEG location can be calculated (if you are analyzing a system that does not have an explicit TSEG register):
TSEG Range is calculated as:
STOLEN
TSEG_SZ
(TOLUD – STOLEN – TSEG_SZ) to (TOLUD – STOLEN)

## Slide 53: Lab: Find TSEG: TOLUD
(TOLUD – STOLEN – TSEG_SZ) to (TOLUD – STOLEN)
(E0000000 - ? - ?) to (E0000000 - ?)
TOLUD = E000_0000h

## Slide 54: Lab: Find TSEG: STOLEN
Next is to find the amount of memory (if any) that has been stolen from graphics
Bits 11:8 determine the amount of graphics memory stolen
In this case it is 0
(TOLUD – STOLEN – TSEG_SZ) to (TOLUD – STOLEN)
(E0000000 - 0 - ?) to (E0000000 - 0)
STOLEN = 0h

## Slide 55: Lab: Find TSEG: TSEG_SZ
And lastly we need to determine the size of TSEG
This will differ based on architecture but for our system it’s 8 bits
(TOLUD – STOLEN – TSEG_SZ) to (TOLUD – STOLEN)
(E000_0000 - 0 - 10_0000) to (E0000000 - 0)

## Slide 56: Calculate TSEG Base/Limit
We plug our known values into:
(TOLUD – STOLEN – TSEG_SZ) to (TOLUD – STOLEN)
(E000_0000h – 0 – 1 MB) to (E000_0000 – 0)
Provides us the range:
DFF0_0000h to E000_0000h
  Technically it’s DFF0_0000 to DFFF_FFFFh
This *should* be the SMBASE address (which is relocatable of course but in all likelihood will be here)
You can also read the SMRR PHYSBASE MSR if it’s supported or on a newer system read the TSEG Base/Limit from the TSEG register
  SMRRs covered in a little bit
E000_0000h
0
STOLEN
TSEG_SZ
1 MB

## Slide 57: Calculate TSEG Base/Limit
The TSEG base address marks the beginning of the protected SMRAM range
Therefore the TSEG base *should* equate to SMBASE
  Or the lowest SMBASE value in a multi-core system, assuming shared SMRAM range
We’ll see in a bit that this isn’t necessarily the case
E000_0000h
0
STOLEN
TSEG_SZ
1 MB

## Slide 58: Memory Map Protection
The location of TSEG is dependent on the values of TOLUD and Stolen Memory
Modifying this value is technically something that an attacker could try to shift the SMRAM region
However these registers can be locked down by either TXT or by the D_LCK bit in the SMRAM register (a key-bit)
  One of these should be used to lock in those memory map values
*I’ve tried it and frozen my system. Optional if you want to try.

## Slide 59: SMRAM Lock-Down
D_LCK is pretty much a necessity and is rarely left unset (5% or so of measured BIOS have D_LCK not set)
When set prevents changes to a lot of registers
Our lab demo laptop isn’t locked thanks to our custom BIOS

## Slide 60: vulnBIOS specific: Viewing SMRAM
If SMRAM is properly locked down this isn’t possible
Assert the D_OPEN bit in the SMRAMC register (D0:F0, offset 9Dh)
Since it’s unlocked, let’s take a look at SMRAM
According to our TSEG calculations it should be located at DFF0_0000h
This should be SMBASE…but is it? Let’s see…

## Slide 61: D_OPEN (or just D_O!)
To help the BIOS configure SMRAM, the chipset provides a means for leaving SMRAM open even when the processor is not in SMM
D_LCK prevents this bit from being asserted
Notes: O_o

## Slide 62: vulnBIOS specific: Viewing SMRAM
Well, there is some binary at DFF0_0000h
EB 38 is a JMP instruction which would take us to DFF0_003Ah
But shouldn’t our code enter at SMBASE + 8000h (DFF0_8000h) instead? Maybe this is just random bits.

## Slide 63: vulnBIOS specific: Viewing SMRAM
Let’s look at address DFF0_8000h
Definitely not executable code
Call it a hunch but let’s look at address DFF0_7EF8h
Recall that the SMBASE field in the state save register is located at offset SMBASE + 8000h + 7EF8h
Let’s see what that shows us

## Slide 64: vulnBIOS specific: Viewing SMRAM
This is the SMBASE value and its value is DFEF_8000h
So SMBASE + 8000h is DFF0_0000h which is our TSEG base
Technically, the SMRAM range is outside of the TSEG protected area

## Slide 65: Unprotected SMRAM Range
We can see that it's outside the range if we go to an address just under DFF0_0000h and write some bytes
Then we can toggle the D_OPEN bit off and on and see that the bytes we just wrote are still present whether SMRAM is open or closed
DFEF_8000h (SMBASE)
DFF0_0000h (SMBASE + 8000h)
Protected Memory
Unprotected Memory

## Slide 66: So how bad is this?
It’s definitely not good! But…
In *this* case the SMI handler neither references nor calls anything in this unprotected range
So it’s “okay” in this case, but could be catastrophic in another
The moral of the story: Ensure that all SMI handler accessed code/data is within the protected memory range
  ITL found multiple bugs in Intel's SMM code where it was accessing data outside the protected ranges, which could consequently be attacker controlled (which led to simple "change a function pointer to jump to my code" type attacks, and could lead to buffer overflow attacks)
DFEF_8000h (SMBASE)
DFF0_0000h (SMBASE + 8000h)
Protected Memory
Unprotected Memory

## Slide 67: Watching the State Save Context Area
While we have SMRAM up it’s kind of interesting* to watch the state context save area change dynamically depending on the processor context when an SMI was generated
Since our laptop generates them 1/s we can see this easily
Not security related, just one of those rare things you otherwise don’t get a chance to see
* Speaking as a nerd, this is the equivalent of watching fireflies in BIOS…

## Slide 68: SMM Entry State
So we’ve seen WHERE the processor enters SMRAM and even saw the initial jump
But what’s the entry state the processor is in when it gets to the entry point?
JMP DFF0_003Ah

## Slide 69: SMM Entry State
Similar to the entry state upon platform reset
However, the General Purpose registers are undefined (unchanged from their values prior to entering SMM)
EFLAGS are zeroed out (bit 1 is reserved and hardcoded)
From Intel Vol. 3. Ch. "System Management Mode"

## Slide 70: SMM Entry State
EIP is set to 8000h
CS Selector is set to SMBASE >> 4
CS Base is set to SMBASE
  Same as at the entry vector, the processor can execute code anywhere in the 4 GB address
CS Limit is set to FFFF_FFFFh (omitted from table)
All segment selectors and bases are set to zero
All segment limits are set to FFFF_FFFFh
From Intel Vol. 3. Ch. "System Management Mode"

## Slide 71: SMM Entry State
With segment Bases and Limits of 0 and FFFF_FFFFh, respectively, the processor can address from 0 to 4 GB of memory address space even in Real Mode
CSBASE + EIP = DFEF8000h + 8000h = DFF00000h
Contrast this with the settings at the reset vector
Despite this superiority, the first thing that will be done is to transition to Flat Protected Mode
Notes: A logical question is why do they do this? And why do they limit the reset vector if they don’t have to?
I have no idea. Legacy I guess.

## Slide 72: SMM Entry State
Debug registers, DR6 and DR7 are read-only in SMRAM
DR7 is cleared upon SMM entry to disable breakpoint traps (bit 10 is hardcoded to 1)
  Prevents a debugger from breaking into an SMI handler if a debug breakpoint is set in normal address space that overlays code or data in SMRAM
From Intel Vol. 3. Ch. "System Management Mode"

## Slide 73: SMM Entry State: Control Registers (CRs)
PG (Paging) is set to zero
  Paging is disabled, all linear addresses are treated as physical addresses
TS (Task Switched) is set to zero
EM (Emulation) is set to zero
  With TS and EM both equal to zero, x87 FPU instructions will be executed
PE (Protection Enable) is set to zero
  Thus the processor enters SMM in 16-bit real mode
All other bits are unchanged from when the SMI was generated
Caching is not explicitly disabled
Most notable bits are high-lighted

## Slide 74: Interrupts in SMM
When the processor enters SMM, interrupts are disabled as follows:
The IF flag in the EFLAGS register is cleared, inhibiting maskable interrupts
The TF flag in the EFLAGS register is cleared, disabling single-step traps
Debug register DR7 is cleared, disabling breakpoint traps
  Preventing an attacker from getting debug access to SMRAM by setting a breakpoint at a normal address that overlaps with SMRAM
NMI, SMI and A20M interrupts are blocked by internal SMM logic
  No, you cannot recursively enter SMM
Software interrupts (INT n) can still occur and maskable hardware interrupts can be enabled by asserting the IF flag
  It is recommended by Intel that SMI handler code not generate interrupts or exceptions
  It’s important to keep SMI handler code inside SMRAM

## Slide 75: NMI Interrupts in SMM
NMI interrupts are blocked when the processor enters SMM
If an NMI request occurs while the processor is in SMM, it is latched and serviced after the processor exits SMM
Only one such NMI will be latched during SMM
If an NMI request is pending when the processor executes the RSM instruction, the NMI is serviced before the next instruction of the interrupted code sequence
Executing an IRET instruction will enable maskable interrupts, in which case the SMI handler had better have setup an NMI handler
  Returns program control from an exception or interrupt handler to a program or procedure that was interrupted by an exception, an external interrupt, or a software-generated interrupt.

## Slide 76: SMRAM and Caching

## Slide 77: Cache Basics
Temporary storage located on the CPU
Accesses to data/instructions in cache are much faster than those to physical memory
Caching is available in all operating modes, including SMM
Caching type for a physical memory range is defined in Memory-Type Range Registers (MTRRs)
Memory Type Range Registers (MTRRs) are a type of MSR (Model-Specific Register) that can be set to specify the type of CPU caching for ranges of physical memory
Configured by BIOS but can also be configured by the operating system as needed
From Intel Vol. 3. Ch. "Memory Cache Control"
Notes: ***This is not going to be a discussion on CPU architecture, for details on caching I recommend 3 sources:
Both the Intel and AMD Optimization Reference Manuals, and Agner Fog’s optimization references

## Slide 78: Memory Caching Types
Physical memory ranges can be defined as having one of these types of caching properties
The only one we’ll discuss is the one that was the subject of the dual discovery by Duflot et al. (SGDN) and then later Wojtczuck et al. (ITL)
  Getting into SMRAM: SMM Reloaded, https://cansecwest.com/csw09/csw09-duflot.pdf
  Attacking Memory via Intel CPU Cache Poisoning, http://invisiblethingslab.com/resources/misc09/smm_cache_fun.pdf
The attack is brilliant in its simplicity
From Intel Vol. 3. Ch. "Memory Cache Control"
Notes: Todo, cite Loic's paper since they technically found it first

## Slide 79: Write-back (WB)
The point of Write-back caching is to reduce the amount of bus traffic between the processor and memory
Reads come from cache lines on cache hits
Writes are performed in the cache and not immediately forwarded to memory
Both read and write misses cause cache fills
Modified CPU cache lines are written back (write-back) to memory at a later time*
*Read the Intel Software Developers Guide Volume 3
Simply put, reading/writing from/to a memory region that uses write-back caching will initially fill a line in the CPU cache
Subsequent reads/writes from/to that address will be from/to cache instead of memory
Until the processor writes-back that cache to memory*

## Slide 80: Some Caching Terminology
A CPU cache is divided up into cache lines
  Each cache line has a line size (like 32 or 64 bytes)
When the processor reads something from memory that is marked as cacheable (as denoted by its memory type per the MTRR), an entire cache line is filled, this is called a cache fill (or cache line fill)
  Partial cache fills are not permitted
  Memory ranges not marked as cacheable are not cached
If the memory location of that read is still cached the next time the processor tries to read it, it can read from cache instead of memory. This is called a cache hit (and is a good thing in terms of performance)
Likewise, a cache miss is simply when a read or write attempt is made to an address that is not cached (and thus will be made from memory).
*Cache is an interesting topic but a detailed explanation is beyond the scope of this course. Agner Fog has written some
great documentation on optimization (and caching). http://www.agner.org/optimize/

## Slide 81: Lab: Cache Poisoning w/ SMM Suppression
This demo requires installing the vulnbios2 bios update*
Open the OSR Loader.exe application on the desktop
  You can alternatively use the instdrv.exe command line utility but this is windows so why bother
In Labs directory, find the “install_vulnbios2.sys” driver
Register the service
Start the service
  you don’t have to stop it or unregister it but you can
When it’s finished, reboot
* I broke one too many protections on this BIOS revision to be able to show subverting the protections

## Slide 82: Lab: Cache Poisoning w/ SMM Suppression
In LPC D31:F0:
Notice that BIOS_CNTL.BLE (bit 1) is asserted
You can try asserting BIOS_CNTL.BIOSWE (bit 0)
Notice it is “immediately” reset back to 0
This bit is being flipped back to 0 in SMM
We cannot write to the BIOS unless this bit is asserted*
You can also open a memory window to DFF0_0000h and see that SMRAM is not open nor writeable
* This is covered in the BIOS Flash section, for now take my word for it.

## Slide 83: Lab: Cache Poisoning w/ SMM Suppression
The steps required to pull off this attack are well-documented, and it is easy to reproduce.
We set up a 1 MB range in physical memory where SMRAM is located and set its memory caching type to Write-back
We next write the RSM instruction to the base of this range which corresponds to SMBASE + 8000h
  The data written will be located in CPU cache
  Because its memory type is Write-back, the CPU will first look to execute from cache
Now the system will exit SMM immediately after entering it
  SMM won’t perform any of those security checks

## Slide 84: Lab: Cache Poisoning w/ SMM Suppression
As Corey Kallenberg pointed out: because SMRAM is charged with the task of protecting the BIOS, if we remove its ability do so then we’re able to overwrite the BIOS
Notice now that BIOS_CNTL.BIOSWE (bit 1) is asserted
We can de-assert and re-assert it at will now
This means we can write to the BIOS now

## Slide 85: Lab: Cache Poisoning (Optional)
We can run our BIOS_CNTL driver that writes 0xDEADBEEF to the base of the BIOS range to prove this fact
Steps:
1) Run Copernicus to dump the BIOS
2) Verify that 0ffset 0x260000* is 0xFFFFFFFF
3) Run the driver to write 0xdeadbeef
4) Re-run Copernicus and see that offset 0x260000 is now 0xDEADBEEF
*Base of the BIOS region in flash. All will be revealed shortly.

## Slide 86: Cache Poisoning IDA “Signature”
For reference, this is what the above steps may look like in asm
Configures an MTRR to set SMRAM range as write-back cacheable
The MTRR pair (numbers) may differ (there are many of them)
  MTRRs are 64 bit registers
The BASE and LIMIT values will overlap SMRAM

## Slide 87: Cache Poisoning IDA “Signature”
You will also see a call to map physical memory
This allocated memory will overlap with a portion of TSEG
Example-specific notes:
This example was performed in a windows driver; the cache type comment refers to the MmCached that you can specify in a call to MmMapIoSpace()
The 1000h is the size of the area we are mapping
Tseg_mb is a PHYSICAL_ADDRESS data structure

## Slide 88: Cache Poisoning IDA “Signature”
tseg is a virtual address mapped to our 1000h byte address range that overlaps TSEG (starting at address DFF0_0000h)
At some point you will see a write to that mapped memory range
For example like that above
After that write, you may see the code generate an SMI, or you may see a write to a PCI device (like asserting bit 0 of PCI D31:F0, offset 0xDC, to enable writes to the BIOS)
It depends on what was written to SMRAM

## Slide 89: The fix: SMRR
The preceding is a great example of how security researchers can influence industry for the better. Damn fine job.
System-Management Range Register (SMRR) was introduced in Intel’s x64 architecture*
  The latest Haswell systems provide more than one SMRR
Provides a PHYSBASE/PHYSMASK pair just like MTRRs
Prevents the kind of attack that we just saw in the preceding example
SMRR restricts access to the address range defined in the SMRR registers
Defines the memory type (caching) for the SMRAM range
SMRRs can be written to only when the processor is in SMM
SMRR takes priority over MTRR in case of overlapping ranges
* This is one of the only architecture-dependent security mechanisms. So far up to this point all has been x32/x64 agnostic

## Slide 90: SMRR
When the processor is in SMM:
  Memory accesses to this range will use the memory type defined in SMRR_PHYSBASE
When the processor is not in SMM:
  Memory reads return a fixed value (0xFF in my experience)
  Memory writes are ignored
  Memory type is Uncacheable

## Slide 91: Verify SMRR Support: IA32_MTRRCAP
SMRR is supported on a system if bit 11 in the IA32_MTRRCAP MSR is set
Verify next that it is being used

## Slide 92: SMRR MSR Number
If you try to read the SMRR of your system, be sure to verify its location using the developers guide (MSR chapter)
The MSR register addresses are non "architectural" and will therefore differ between architectures
  That’s why they are called Model-Specific Registers
RW-E does not appear to handle exceptions well since reading the wrong MSR will crash your system
  As of latest version
For our lab E6400 (Core2Duo) this is ours

## Slide 93: Multiple SMRAM Ranges, One SMRR
As we know, there can be more than one SMRAM range used
  Each core could theoretically implement an SMBASE in a completely separate memory range (although this would be foolish)
  The compatible range (A_0000 – B_FFFFh) is used alongside TSEG
However, in the Intel Software Programmers Guide, Chapter 35 (MSR’s), each architecture is listed as having just one SMRR
So this means that even when SMRRs are used, there will still be one range (likely the compatible range) that will still be subject to cache attacks
Likely this range is unused, but not necessarily
If more than one SMRAM range is actually used on a system which provides just one SMRR, then at some point the SMI handler must call the WBINVD instruction
Intel’s Haswell architecture (I believe) provides more than one SMRR now

## Slide 94: Intel Guidelines for Caching
Intel provides 3 guidelines for the location of SMRAM so that cache coherency is always guaranteed (meaning that what is in cache matches what is in memory
They don’t mention the use of SMRR in these guidelines, but if SMRR is not implemented, then even following these guidelines will endanger SMRAM
1) Place SMRAM in a dedicated section of system memory that the OS and applications are prevented from accessing. If put here, then the SMRAM caching type can be WB cacheable.
  Placing SMRAM in TSEG matches this criteria (TSEG is next to stolen memory but does not equal stolen memory)
  Being able to (securely) cache SMRAM is desirable for performance gains
2) Place SMRAM in a part of system memory that overlaps an area that is used by the OS (video memory, for example) but mark it as Uncacheable
3) Place SMRAM in a part of system memory that overlaps an area that is used by the OS but explicitly write-back and invalidate the caches upon entering and before exiting SMM.
Notes: ***This is not going to be a discussion on CPU architecture, for details on caching I recommend 3 sources:
Both the Intel and AMD Optimization Reference Manuals, and Agner Fog’s optimization references

## Slide 95: SMM Misc: I/O Trapping
Enables the execution of the SMI handler upon execution of an IN/OUT instruction to a specified IO range
Bit 0 is R/W so it does not appear that this register can be locked down
It is limited to I/O address space

## Slide 96: SMI Suppression

## Slide 97: SMI Suppression
SMM stands as the first line of defense for protecting the BIOS flash from being overwritten
  We’ll cover how in the flash BIOS portion of the course
What if the attacker simply suppressed SMI from being generated?
They can, if the system isn’t locked down properly:
I/O Controller Hub Family 9

## Slide 98: SMI_EN: SMI Control and Enable Register
Located in the Power Management IO Registers (memory-mapped at PMBASE defined in LPC D31:F0)
The SMI_EN register can enable or disable some very specific instances of SMI# or globally enable/disable all SMI#
Shown above is the Global Enable/Disable for SMI#

## Slide 99: SMI_EN
We can disable the generation of SMI# on writes to IO port 0xB2
And a slough of others (BIOS_EN refers to BIOS being able to receive ACPI “messages”, it has nothing to do with enabling/disabling BIOS itself)

## Slide 100: SMI_EN
SMI_EN provides a lot of control over the generation of SMI#
It can also enable/disable that periodic generation of SMI#
You get the idea…

## Slide 101: Demo: SMI Suppression
As we know, we (should be) unable to assert bit 0 in the BIOS_CNTL register located in LPC D31:F0, offset DCh
Let’s “fix” that!
BIOS_CNTL register

## Slide 102: Demo: SMI Suppression
Locate the PMBASE address from LPC D31:F0, offset 40h
This is mapped to the I/O address space, as indicated in the Base Address register description

## Slide 103: Demo: SMI Suppression
In this case we can see it is mapped to I/O starting at address 0x1000
Open up an I/O ports window and enter 0x1000
Be sure to check ACPI Power Management Base
On some systems not doing this causes lockups or system crashes

## Slide 104: Demo: SMI Suppression
The bit to suppress global SMI# is at bit 0 in the SMI_EN register located at PMBASE + 30h
It looks like uninitialized space, but everything is enabled
Just not locked down

## Slide 105: Demo: SMI Suppression
Commence SMI# suppression!
De-assert bit 0 so that SMI_EN is FFFF_FFFEh

## Slide 106: Demo: SMI Suppression
Now with SMI# suppressed we can enable writes to the BIOS flash by asserting bit 0 in the BIOS_CNTL register
We’ll cover this in more detail in the next section
BIOS_CNTL register

## Slide 107: Demo: SMI Suppression
Notice that bit 0 remains asserted now whereas before disabling SMI# it would have been reset to 0
Now we can write to the BIOS. This is very bad.

## Slide 108: Demo: SMI Suppression
Running the write_bios_base_deadbeef.sys writes to the BIOS base to prove this point

## Slide 109: Demo Video: Charizard
Ring0 can modify authenticated EFI Variables, which allows trivial bypassing of Secure Boot
  We’ll cover this in the UEFI secure boot portion of the class. For now just take my word for it: this is not good
Notes: Note, this is from our public released charizard talk

## Slide 110: SMI Suppression
As we’ll see in the next section, there is one secondary defense that could still work to prevent an attacker from being able to flash the BIOS under these circumstances
  However they can’t be used to protect the UEFI variables because those must always be writeable
Locking down the SMI_EN register is something that vendors don’t really know about:
3216 of 8005 (~40%) systems measured did not have SMI_LOCK set
  The numbers are much higher if you rollback the BIOS to a vulnerable revision, which is typically permitted

## Slide 111: SMI Suppression Prevention 1: GEN_PMCON1
GEN_PMCON1 is located in the LPC D31:F0 Power Management registers
The vendor must (must must!) assert SMI_LOCK in the GEN_PMCON_1 register
Don’t give attackers the option of suppressing SMI#
Especially since the system depends on SMM to protect the BIOS Flash!!!

## Slide 112: SMI Suppression Prevention 2: BIOS_CNTL.SMM_BWP
We’ll cover this register during the BIOS flash portion of the course
Raises the security level of the platform
Suffice to say this is a very useful (newish) feature
  That isn’t utilized very often

## Slide 113: SMM Lockdown Summary
Although these may generally only be implemented by the vendor, you can verify most of these
Use TSEG
Ensure entire SMRAM range is contained in the protected space
SMI handler code should not execute code outside the protected memory range
Don’t use interrupts in SMM, unless you explicitly WBINVD the cache before generating an interrupt
Ensure D_LCK is set to lock down both memory-mapping registers as well as SMRAM
Verify SMRR are supported
Verify SMRR are used
Verify SMRR range overlaps/matches TSEG
Verify SMM_LOCK bit is asserted to prevent an attacker from suppressing SMI#
Verify the SMM_BWP bit is set in the BIOS_CNTL register to permit writes to flash only when processor is in SMM

## Slide 114: SMM Conclusion
Holds a lot of responsibility in protecting the system
  Protects the BIOS flash
  Protects itself, because it is instantiated by the BIOS from binary on the BIOS flash
So it is very fragile in case of a writeable BIOS
  It is not difficult to locate and “carve” out the SMI code module and replace it with a malicious one
  Once written to BIOS the attacker can lock down the once-vulnerable system
  Which highlights a general problem with tools like Copernicus. We’ll touch on this at the end of the Trusted Computing section
Bottom line:
If the attacker can write to the BIOS, they can modify SMM (and a lot of other stuff, unlocking protections, etc.)
Therefore, the most important thing to lock down is the SPI Flash, first and foremost.
  The protection of which relies first and foremost on SMM