## Slide 1: Advanced x86: BIOS and System Management Mode Internals
John Butterworth & Xeno Kovah
Part 3: Flash BIOS

## Slide 2: All materials are licensed under a Creative Commons “Share Alike” license.
http://creativecommons.org/licenses/by-sa/3.0/
Attribution condition: You must indicate that derivative work
"Is derived from John Butterworth & Xeno Kovah’s ’Advanced Intel x86: BIOS and SMM’ class posted at http://opensecuritytraining.info/IntroBIOS.html”
Notes: Attribution condition: You must indicate that derivative work
"Is derived from Xeno Kovah's ’Introductory Intel x86: Assembly, Architecture, and Applications’ class"

## Slide 3: BIOS Flash Overview
Everything we have talked about so far, although harmful to a system, isn’t persistent unless you can write to the BIOS
But one of the goals an attacker has in establishing a presence in the system is persistence
To achieve persistence, the attacker will have to figure out a way to write to the BIOS flash so that upon every reboot, his presence is still there
Using Copernicus we have measured systems multiple organizations, so far we have found that ~55% of systems measured have BIOS’ which is over-writeable

## Slide 4: BIOS Flash Location
BIOS can reside in one of 3 locations:
Firmware Hub (FWH)
  Older technology but still supported in the newest chipsets (8-series at the time of this writing)
SPI Flash
  Most likely location
PCI
  intended for debugging or recovering from a corrupted BIOS

## Slide 5: Boot BIOS Flash Location
The boot destination is decided by the configuration of the following pins on the ICH/PCH*
Pins are sampled at power-up to determine location of BIOS
Intended for static configuration
PCI boot is intended only for debugging or recovering from corrupt BIOS (so not necessarily static)
* References to ICH/PCH mean applicable to both legacy and modern chipsets

## Slide 6: Lab: Find BIOS Boot Destination
To programmatically find where your BIOS is configured to boot from, you can also view bits 11:10 in the General Control and Status Register (GCS)
Located at memory-mapped offsets 3410-3413h in the Chipset Configuration Registers
Chipset Configuration Registers are mapped starting at the address held by RCBA…you know, RCRB? :)
Verify GCS location on your datasheet if not using the class E6400.
01b SPI (typo in datasheet)

## Slide 7: Quick Note: RCBA/RCRB
The Root Complex Register Block (RCRB) decode range is located in the Root Complex Base Address (RCBA) register located in the LPC (D31:F0, offset F0-F3h)
The root complex is PCI-Express related. It connects the processor and memory to the PCI Express devices.
  If you want to know more about the inner workings of PCI Express, there are a number of good sources, such as (Darmawan):
  http://resources.infosecinstitute.com/system-address-map-initialization-x86x64-architecture-part-2-pci-express-based-systems/
You know the drill!

## Slide 8: Lab: Find BIOS Boot Location
Locate RCRB:
Bit 0 is just an enable bit (the nibble this bit is in is still part of the address, but change it to 0)
Here the RCRB begins at FED1_8000h
The GCS register is located at in the chipset configuration registers.
At RCRB + 3410h = FED1_B410h
The root complex base address will differ on different systems.
Notes: If you answer “undetermined”, pat yourself on the back and move to the next slide. If you said what the bits indicate well you are still probably correct.

## Slide 9: Lab: Find BIOS Boot Location
GCS at FED1_B410h yields the following value on our lab system:
00C0_0440h
Bits 11:10 are 01b which indicates that this BIOS boots from SPI
But how can we trust what this says? We’re not actually sampling the Controller’s pins in this register
Bits 11:10
Notes: If you answer “undetermined”, pat yourself on the back and move to the next slide. If you said what the bits indicate well you are still probably correct.

## Slide 10: Lab: Change BIOS Access Destination
Notice these bits are R/W?
You can change the destination for BIOS accesses
Likely this is to help the system recover from a corrupted BIOS
But it could be certainly misused as well
Note just to be clear: The bits in GCS alter accesses to the BIOS *only* after the BIOS has begun booting
  Chipset Configuration registers must be mapped to memory, etc.
The functional straps are physical pins which cannot be altered and decide the BIOS Boot Location

## Slide 11: Lab: Change BIOS Access Destination
Bring up a memory window and go to an address which shows the memory-mapped BIOS (like FFFF_FF80h which will show us the entry vector)
You should see the BIOS in memory

## Slide 12: Lab: Change BIOS Access Destination
Modify the GCS register to 00C00C40h, bits 11:10 are 11b now which point the device to the LPC
On our lab system the LPC has no firmware BIOS so this translates to reads of all 1’s (0xFF)
Your personal system may differ and you may actually see valid binary here.

## Slide 13: Lab: LOCK BIOS Access Destination
Intel provides a way to lock down the destination of BIOS accesses
When bit 0 in the General Control and Status Register (GCS) is set, bits 11:10 become Read-Only
The BIOS should lock this down!

## Slide 14: Lab: Change BIOS Access Destination
Set bits 11:10 in the GCS register back to their original values (01b for SPI)*
Assert bit 1 in GCS, now GCS is 00C00441h
Now find that bits 11:10 are fixed in place
*Or leave them pointing to nothing, this is not permanent and nothing a reboot won’t reset

## Slide 15: A Word About This
This only affects direct accesses to BIOS flash
Programs (like Copernicus or Flashrom) that read directly from the BIOS flash using the SPI programming registers (for example) will still successfully read the BIOS binary from the chip
Notes: When we program the SPI registers, we aren't accessing that memory-mapped space. We are reading data in and out of a buffer, accesses to that buffer do not derive from the memory-mapped range.

## Slide 16: Firmware Hub (FWH)
Provides register-based R/W protection for each code/data storage block
Has hardware write-protect pins for the top boot block and the remaining code/data storage blocks
Contains a Random Number Generator (RNG)
More than one FWH device can be supported
Operates at 33 MHz (synchronous to the PCI bus)
Has a lot of pins compared to SPI
Intel 82802AB/82802AC Firmware Hub (FWH)
It's a me! Mario!

## Slide 17: Firmware Hub (FWH)
Memory-mapped interface
Programmable Erase, Read, Write commands
Each block can be locked down to prevent Reads and/or Writes
Firmware hubs are rare (at least in modern PC’s) and I have never seen one
Sample FWH datasheet:
http://download.intel.com/design/chipsets/datashts/29065804.pdf
If you ever encounter a system with a firmware hub email me and tell me the make/model please
Intel 82802AB/82802AC Firmware Hub (FWH)

## Slide 18: Serial Peripheral Interface (SPI)
SPI controller can support 1 or 2 devices for 32 MB maximum addressable space
Lower cost alternative (per Intel datasheet)
Memory-mapped programming interface offset from RCRB (consult your datasheet for its exactly offset)
Intel’s ICH/PCH implements an SPI interface as an alternative interface for the BIOS flash device.
Used as a replacement for the Firmware Hub (FWH) on LPC
SPI is required in order to support Active Management Technology (AMT), Gigabit Ethernet (GbE), and others.
Each SPI flash device can be up to 16 MB (224 bits)
Typically 8 pins, can be 16
*Based on datasheet information and that the Flash Address Register accepts addresses occupying bits 24:0

## Slide 19: SPI Overview
SPI protocol can support data rates up to 100 MHz
  Intel’s implementation is configurable to operate at either 20 MHz or 33 MHz (or 50 MHz on the newer PCI Express systems)
Intel abstracts most of the low-level SPI protocol from you
SPI protocol is not a fixed standard
  Different chips will support different commands and so forth
Intel defines a set of minimum requirements for a chip to support.
  Likely though each chip will support more than just that bare minimum
So we’ll be covering Intel’s implementation and interface to SPI, not really the SPI protocol itself (they intertwine somewhat of course).

## Slide 20: SPI Operating Modes
Since I/O Controller Hub version 8, the SPI flash has been able to support 2 distinct operating modes:
Non-Descriptor Mode (RIP, deceased ’09)
  IT LIVES! (On embedded devices like MinnowBoard!)
  In ICH7 this is the only supported operating mode
Descriptor Mode
  Since ICH8 (so ICH8, ICH9, ICH10, and PCH)
For systems that have a Platform Controller Hub device (PCH), non-descriptor mode has been phased out and is no longer supported
Notes: I know I read something to this effect, need to find it.

## Slide 21: Descriptor Mode
Enables chipset features like:
  Integrated Gigabit Ethernet, Host processor for Gigabit Ethernet Software, Active Management Technology
Provides support for two SPI flash chips
Divides the SPI flash into regions
Provides hardware enforced security restricting region access
Chipset Soft Strap region provides the ability to use Flash NVM as an alternative to hardware pull-up/pull-down resistors for both ICH and PCH
  On reset, the controller hub reads the soft strap data out of the SPI flash
Can be programmed (at a minimum) using the commands specified in the Intel ICH/PCH datasheet
  But each chip can support additional commands, not very standardized
Notes: *** Ok that;s interesting…
**** Standardized – the JEDEC ones?

## Slide 22: Memory Mapping: Descriptor Mode
All of the flash chip is mapped to high memory
In Descriptor Mode, only the BIOS region of the flash is readable in memory
All other regions return 0xFF on reads
  We'll get to the other regions in a bit
Memory
4GB
Flash Contents
Flash contents that are viewable in Memory
BIOS Region

## Slide 23: Non-Descriptor Mode
Best described by its lack of features (as compared to Descriptor mode)
The entire flash is used for BIOS (this does not mean the BIOS will be larger)
Security features available in Descriptor mode are not available in Non-Descriptor mode
  The BIOS/CPU can read/write to the flash without restriction
Therefore there is also no support for Gb Ethernet, Management Engine, or chipset soft straps
Interesting quote in Intel’s ICH datasheet (10, in this case): “[in Non-Descriptor Mode], Direct read and writes are not supported.”
‘Non-Descriptor Mode == !Descriptor Mode’
No longer a viable option on the newer PCH systems, since they require a valid flash descriptor

## Slide 24: Memory Mapping: Non-Descriptor Mode
In Non-Descriptor Mode the entire flash contents are visible in memory (more than just BIOS, if any more is present)
If flash is < 16 MB and the FWH decoders are enabled in LPC, you will see the BIOS mapped repeatedly (think ribbons) at high memory
  A 4MB BIOS is mapped 4 times in the high 16 MB of memory space
A flash device in descriptor mode that has its descriptor signature “corrupted” will be viewable in memory in its entirety
  But the descriptor signature is protected, so that would require physical flash access to corrupt
Memory
4GB
Flash Contents
Flash Contents Readable in Memory
Entire Flash
4GB – 16 MB
4GB – size of flash (MB)
Notes: But note that you shouldn't be able to corrupt the descriptor for the OS, since it *should* be unconditionally write protected on any correctly configured system (I don't think we've found any that have vulnerable descriptors)

## Slide 25: Non-Descriptor Mode Memory Mapping
Example of 4 MB device in “non-descriptor” mode mapped to high 16MB of memory
“Invalid” Flash Descriptor
0FF0A55Bh
instead of 0FF0A55Ah

## Slide 26: Why is some of the chip visible in memory in one mode but not the other?
Has to do with the type of flash access as well as permissions to read that memory:
There is an SPI “rule” that states:
  Every SPI Master has direct read access to it’s own region only
  Direct Access refers to memory reads in mapped memory
  Thus the BIOS Master can read the BIOS region in memory (mapped to high mem at 4 GB)
In Descriptor mode, the SPI flash is divided into regions
  BIOS region, Flash Descriptor, etc. (we’ll cover in more detail soon)
Therefore, in Descriptor Mode, only the BIOS region can be seen in high mapped-memory
In Non-Descriptor mode, there is no concept of regions
  It’s just “the BIOS”
So therefore, the entire “BIOS” (entire flash) can be seen in memory when the SPI flash is in Non-Descriptor mode

## Slide 27: Flash Accesses: Direct & Register
Direct Access
  This applies to memory accesses (mapped to high-memory)
  Masters are allowed to read only their own region
    CPU/BIOS can read the BIOS region
    Management Engine can read only the ME region
    GbE controller can read the GbE region (GbE software must use the programming registers)
Register Access
  Access a region by programming the base address registers
  Register accesses are not allowed to cross a 4 KB aligned boundary
  Cannot execute a command that may extend across to a second SPI flash (if present)
  Software must know the SPI flash linear address it is trying to read
Notes:   (this slide seems duplicative? May delete)
  When you read the flash that is mapped to upper 4GB of memory, this is direct access.
  We will get into actual SPI programming in a future Advanced class, for now we just want to understand that there is an interface and how to use some pre-made tools for forensics analysis
*** Is it the flash controller that limits this? Or the ICH decoder?

## Slide 28: Register Access: SPI Base Address Register (SPIBAR)
SPI extends it’s Base Address Registers (BARs) to memory starting at an address called SPIBAR
SPIBAR is offset from the Root Complex Register Block (RCRB)
The offset from RCRB is chipset-dependent, but will be listed in the SPI section of the datasheet
SPIBAR
Offset | Name | Value
F0h | RCBA | FED18000
LPC Device | B0:D31:F0
ICH (same on PCH)
RCRB
SPIBAR
offset
memory
Notes: http://superradnow.files.wordpress.com/2012/09/spy.jpeg

## Slide 29: Lab: Locate SPIBAR
Per your datasheet, the SPI host interface registers (SPIBAR) is located at an offset from RCRB
In the Mobile 4-Series chipset on our lab laptop, SPIBAR is located at:
RCRB + 3800h = FED1_B800h
déjà vu!

## Slide 30: SPI Regions
Intel has left room for additional regions
The only ones required are the Flash Descriptor region and the BIOS region
They are not listed in the order in which they will appear on the flash chip:
  Flash Descriptor will always be first, as listed, but BIOS will always be last so it ends at 4 GB of memory address space
Added in ICH9
Required
Required
Notes: *** I think platform data was added for ICH9? ICH8 had only 4 regions I think.

## Slide 31: Determining SPI Regions
You can determine the regions on your flash by reading the FREG(n) registers in the SPI Base Address Registers (SPIBAR + {54 to 64h})
FREG0 to FREG4, each 32 bits
If the Base is higher than the limit, the region is unused
Notes: *** I think platform data was added for ICH9? ICH8 had only 4 regions I think.
Note: I wanted to do a "Fred + Greg = FREG!" picture, but there's literally no famous gregs! Just enter "Greg" into google images and see for yourself!

## Slide 32: Flash Descriptor
Defines most (but not all) of the flash protection that are supported by the Controller Hub
  Not defined in flash descriptor:
    BIOS Range Write Protection
    SMI# Global Write protection (described elsewhere)
    Logically OR’d together, if either are set then access is blocked
The flash descriptor registers used to be documented in the I/O Controller Hub datasheets
Now, in the PCH datasheets, the descriptor sections are not listed. The GbE portion of the Descriptor is, however
  (this is not the same thing as the GbE PCI device)
Must be written during the manufacturing process and set to Read-Only when it leaves the manufacturer, per Intel
  Sometimes (rarely) the Flash Descriptor itself is vulnerable

## Slide 33
Signature 0FF0A55Ah denotes the device has a valid descriptor and is therefore operating in Descriptor mode.
Signature offset is located at 0 on ICH8, ICH9, and ICH10
In PCH it has been moved to 0x10 and bytes 0 thru 0x0F are Reserved
Pictured: ICH 10 Flash Descriptor
This "Flash Descriptor" structure is what's read by the ICH/PCH in order to populate and expose the information via RO registers (like FREG0) in SPIBAR

## Slide 34
ICH8
ICH9, ICH10
PCH
Renamed
Offset shifted
Combined…
Evolution of the Flash Descriptor from ICH to PCH
ICH 8, 9, 10 are identical
Still 256 bits
Still 256 bits
Notes: Maybe put this in the Appendix for reference and keep just the PCH one here in actual SPI section

## Slide 35
The registers of the Flash Descriptor used to be documented fully in the I/O Controller Hub datasheets.
In the Platform Controller Hub datasheets, however, the Descriptor offsets and registers are no longer described.
For this reason, I will use the image of the flash descriptor as taken from ICH10.
When describing the protection mechanisms provided by the flash descriptor, I’ll point out how they differ between ICH revisions where applicable
Remember, this isn’t an exercise in memorization but in acquiring new awareness and understanding, with that you can fill in details as they change in the future.
The functionality described will be present, even if the offsets change in the future.
ICH10 used as example
FDBAR

## Slide 36: Signature
Signature 0FF0A55Ah identifies a valid flash descriptor
A valid flash descriptor indicates the SPI flash is operating in Descriptor mode
PCH and Management Engine each require a valid flash descriptor
Located at FDBAR + 0000h
  FDBAR defined in bits 12:0 in FREG0 (located in SPIBAR)
Signature offset is located at 0 on ICH8, ICH9, and ICH10
In PCH it has been moved to 0x10 and bytes 0 thru 0x0F are Reserved
FDBAR
Notes: FDBAR = food bar = http://www.grocery.com/wp-content/uploads/2013/05/organic-food-bar-active-greens.jpg

## Slide 37: Descriptor Map
Describes the data structure of the Flash Descriptor
number of sections in the descriptor
pointers to these sections as well as the size of each section
# of physical SPI flash chips present
FDBAR
FLMAP0
FLMAP1
…

## Slide 38: Component
Identifies the different flash chips themselves and their capabilities
Read/Write/Erase clock frequencies
Even if there are 2 SPI chips, there is still just a single component section
The component section contains the Flash Invalid Instructions Register which says which instructions will be blocked from execution by the hardware

## Slide 39
Defines opcodes that will be prevented from running on the chip by the flash controller hardware
Chip Erase (opcode 0xC7 is a good one to block)
FLILL register is constant across ICH8, ICH9, ICH10 and appears to be the same on PCH*
  Same location (FCBA + 004h), same bit meanings
*Based purely on my analysis of BIOS dumps on machines running PCH
Yo

## Slide 40: Note on SPI Instructions (opcodes)
Each ICH/PCH datasheet defines a minimal set of SPI commands that a chip must support
  H/W Sequencing
  Interoperability with Intel platform
This table can serve a reference to identify any opcodes that are listed in the FLILL register
However, each serial flash device may have unique capabilities and commands
ICH 10 Required Opcodes
*Write Enable looks interesting doesn’t it? A future Advanced course goes into SPI Programming

## Slide 41
Supported opcodes on an Atmel AT25DF321A SPI Serial Flash
Taken straight from Atmel’s datasheet
Supports more than the minimum set required by Intel
Notice it supports more than one Chip Erase command
FLILL register must be filled out with these opcodes in mind, not just those that Intel lists
http://www.atmel.com/Images/doc3633.pdf

## Slide 42
Looking at the Flash Invalid Instructions Register from the Copernicus BIOS dump, we can see that none are defined
Although only 4 opcodes can be black-listed here, it’s still a setting that should be used
And the SPI Flash vendor’s datasheet should be taken into account when defining forbidden opcodes
I don’t recall any other source that has provided this recommendation
FLILL = 00000000h

## Slide 43: Region
Identifies the different regions of the SPI Flash (BIOS, Mgt Eng, etc.)
  Not to be confused with defining the flash descriptor map.
Each FLREG register (0-4) has a base and a limit, each corresponding to the range of that particular region
  FLREG0 = Flash Descriptor
  FLREG1 = BIOS
  FLREG2 = ME
  FLREG3 = GbE
  FLREG4 = Platform Data
Disabled/unused regions will have a base of 1FFFh and a limit of 0000h
  Can determine what regions are active
  If BIOS region is inactive, then the BIOS is located on the FWH

## Slide 44: Keeping it straight
FLREG0-4 are what's in the Flash Descriptor. The data from the Descriptor is then exposed through FREG0-4 registers.

## Slide 45: Master
Defines the Read/Write capabilities that each Flash Master has with respect to each of the SPI regions, including the flash descriptor
Each SPI Master has a register that defines these permissions called the Flash Master register
  Permissions apply only to register access
Also describes if and how the SPI flash is logically divided into partitions
  Can be divided into one or two partitions, Upper and Lower
  Each partition, separate from regions, can have different attributes
Section base is located at FMBA + 000h
  Defined in FLMAP1 (FDBAR + 08h, 0:7)

## Slide 46: Flash Master Permissions
Register layout is identical for each of the three masters
Register location and layout is also identical across ICH8, ICH9, ICH10
Appears to be identical on PCH as well*
*Based on my analysis of SPI serial flash dumps
Should never be set anywhere!
Notes: FD region needs to be made write-protected from ALL masters during manufacturing. Never supposed to change.

## Slide 47: Flash Master Permissions
The requestor ID of the master attempting to access a region must match that of the defined requestor ID
  2-Byte value
  CPU and ME must have requestor ID’s of 0h
  GbE must have a requestor ID of 0218h
Each master will always have Read/Write permission to its own region
  CPU/BIOS will always be able to read the BIOS region of the SPI flash, and so on.
  This is by default and hardcoded by Intel
BIOS
GbE
ME
Notes: http://img4.wikia.nocookie.net/__cb20110829153234/marvel_dc/images/4/48/Flash_Sega_Master_System.jpg

## Slide 48: Example: FLMSTR meanings
Based on analysis of the Descriptor Map (FLMAP offset 8h), we have identified that the Master section begins at offset 60h of the Serial Flash (06h is left-shifted 4 bits).
  FLMAP = 12100206h (bits 7:0 define Flash Master location)
FLMSTR1 (CPU/BIOS) = 1A1B0000h
FLMSTR2 (Mgt Engine) = 0C0D0000h
FLMSTR3 (GbE) = 08080218h
FLMAP1 (7:0)
defines Master
section location
at 60h
Master Section
*HxD doesn’t let you view the words in 32- bit format (with little-endian interpretation)
Notes: Create a tool that analyzes a dumped binary, rather than reading from the chip. SPI programming should be handled in the advanced course.
Pop quiz: what Controller Hub family is this dump from?

## Slide 49: FLMSTR1 (CPU/BIOS)
FLMSTR1 (CPU/BIOS) = 1A1B0000h
Therefore CPU/BIOS has the following privileges:
Write (bits 28:24)
  Can write to the Platform Data region of SPI Flash
  Can write to the BIOS region of SPI Flash
  Can write to the GbE region of SPI Flash
Read (bits 20:16)
  Can read the Flash Descriptor of SPI flash
  Can read the BIOS region of SPI flash
  Can read the GbE region of SPI flash
Master Section
*Note: The FLMAP0 register defines 03h + 1 SPI regions, therefore there is no Platform Data region on this SPI flash.

## Slide 50: CPU/BIOS Permissions = 1A1B0000h
1
1
0
1
0
1
1
0
1
1
*Note: The FLMAP0 register defines 03h + 1 SPI regions, therefore there is no Platform Data region on this SPI flash.
1
A
1
B
0000
Notes: Just an alternate slide format to the one prior.
I think I like the prior one better. Not sure.

## Slide 51: ME Permissions = 0C0D0000h
*Note: The FLMAP0 register defines 03h + 1 SPI regions, therefore there is no Platform Data region on this SPI flash.
0
1
1
0
0
0
1
1
0
1
0
C
0
D
0000

## Slide 52: GbE Permissions = 08080218h
*Note: Requestor ID 0218h is required on ICH8, ICH9, and ICH10 systems, in PCH this is 0118h
0
1
0
0
0
0
1
0
0
0
0
8
0
8
0218
Notes: Just an alternate slide format to the one prior.
I think I like the prior one better. Not sure.

## Slide 53: Soft Straps
First implemented in ICH8
  In PCH, both regions are combined into a single PCH Soft Straps section
Soft Strap data is read out of the SPI device prior to de-asserting a reset (power-on, in layman’s terms)
Configure specific functions within the chipset before the BIOS or any other software can intervene
The specific details regarding the implementation of Soft Straps are located in Intel’s confidential SPI programming guides
Notes: The soft strap data is read prior to the de-assertion of reset to both the Mgt. Engine and the host system.
Systems exit sleep mode and such via a de-assertion of a reset (different types, SLP_SUS# for instance).

## Slide 54: OEM Section and Descriptor Upper MAP
OEM Section
  *CH does not read the OEM information
  256 bytes (ICH8, ICH9, ICH10, and PCH (up thru 8-series PCH1)
Descriptor Upper MAP
  Describes the Base and length of the Management Vendor Specific Component Capabilities (VSCC) Table
  Base address is at FDBAR + EFCh (ICH8, ICH9, ICH10, and PCH2)
    Recall FDBAR is offset 10h on the flash chip on PCH, 0h on all others
1 Most recent PCH at the time of this writing
2 Based on my analysis of BIOS binaries
FDBAR

## Slide 55: Management Engine VSCC* Table
Contains the JEDEC ID of the Flash Chip
  Identifies the Vendor and Device ID of the SPI serial flash
Describes the different attributes an SPI partition can have (Upper or Lower)
  Based on the value defined in the FPBA flash descriptor register in the Master section
  If SPI is defined as having one single partition, then only the attributes defined for the Upper partition are used.
*VSCC = Vendor Specific Component Capabilities

## Slide 56: Flash Protection
With no Flash Descriptor present, the only mechanisms to lock the flash are:
  BIOS Range Write Protection
  SMM Write Protection (aka Global Write Protection)
The reference to FWH Sector Protection yields no results in any datasheets. I am assuming it is related to the R/W control shown in the sample FWH register map at the beginning of the BIOS Flash section

## Slide 57: Flash Protection Mechanism #1
Covering this first because I believe it to be your first line of defense to protect your BIOS flash from writes
Applies to the entire flash chip (Global Flash Protection)
Provides SMM the ability to determine whether or not a request to unlock the BIOS flash for writing will be permitted
This protection is provided by the chipset (not on the flash itself)
Notes: *** There is literally no info on FWH Sector Protection…not even in the really old ICH datasheets nor BIOS Ninjitsu
*** Verify writes to PD section are still blocked…
  Just to hammer it home: It is really important to lock down SMRAM!!!

## Slide 58: Global (or SMM) Write Protection
On MCH/ICH systems, bits 7:5 of the BIOS_CNTL are reserved
BIOS_CNTL is located in the LPC device (D31:F0, offset DCh)
These protections would also apply to the Firmware Hub (FWH) if the BIOS were located there.

## Slide 59: ICH/PCH Chipset SMM-derived Write Protection:
BIOS_CNTL.BIOSWE (bit 0) enables write access to the flash chip
  Always R/W
BIOS_CNTL.BLE (bit 1) provides an opportunity for the OEM to implement an SMI to protect the BIOSWE bit

## Slide 60: How it works
BIOS_CNTL.BIOSWE = 1
BIOS_CNTL
BLE = 1
BIOSWE = 0
Privileged Application
Privileged app wants to write to the SPI flash, sets BIOS_CNTL.BIOSWE to 1
  The only reason privileges are needed is to execute the in/out instructions
SMM

## Slide 61: How it works
BIOS_CNTL
BLE = 1
BIOSWE = 1
SMM
SMI
The BIOS_CNTL register has the BIOS Lock (BLE) enabled
Asserting BIOSWE while BLE is set generates an SMI#
  SMI# is initiated by the Chipset (ICH)
The processor transitions to System Management Mode
Privileged Application

## Slide 62: How it works
BIOS_CNTL
BLE = 1
BIOSWE = 1
SMM
No no no, this will never do…
SMI Handler
A routine in the SMI handler explicitly checks to see if BIOS_CNTL.BIOSWE is set
Privileged Application

## Slide 63: How it works
BIOS_CNTL
BLE = 1
BIOSWE = 0
SMM
Much better
Zeroes BIOSWE bit
The SMI handler flips this bit back to 0, disabling writes to the serial flash
  Since updates should be applied only by SMRAM, SMRAM knows that unless it flipped this bit, this bit shouldn’t be flipped.
Privileged Application

## Slide 64: How it works
Heh heh heh
SMM
BIOS_CNTL
BLE = 1
BIOSWE = 0
Aw
From the app’s perspective, it appears the BIOSWE bit was never even asserted.
Of course this only works if:
  BLE is asserted/enabled
  There is a SMI handler explicitly checking/resetting the BIOSWE bit
  SMIs cannot be somehow suppressed (you already saw 1 way)
Privileged Application
Notes: The nerd in me wants to remove SMM’s taunting laugh because once the CPU exits SMM, SMM is no longer able to “gloat.” However, I like the gloating SMM.

## Slide 65: Lab: BIOS_CNTL Testing
Look at the BIOS_CNTL register in the LPC device
BIOS Lock Enable (BLE) bit 1 is not asserted
This means any application privileged enough to either map the PCI Express configuration space or perform port I/O can assert BIOSWE to enable writes to the BIOS flash

## Slide 66: Lab: BIOS_CNTL Testing
First let’s establish the fact that we cannot write to the BIOS flash without first enabling Writes via BIOS_CNTL
We’ll try to write to the BIOS flash with BIOSWE disabled (set to 0)

## Slide 67: Lab: BIOS_CNTL Testing
Run write_bios_deadbeef.sys with OSR Driver Loader
This cleverly-named app will attempt to write 0xdeadbeef to the base of the BIOS region at FLA 0x260000
Run Copernicus.bat to dump the flash contents
Open Copernicus_BIOS.bin in the C:\ drive and go to address 0x260000
This should fail, as evident by the 0xFFFFFFFF still at flash address 0x260000

## Slide 68: Lab: BIOS_CNTL Testing
Now let’s establish that we can write to the BIOS by simply enabling BIOSWE bit 0
Note: If Flash Master permissions provide write-access to the CPU/BIOS, we would be able to write to other regions as well
Set BIOSWE to 1
BIOS_CNTL should now equal 0x09
  0000 1001b

## Slide 69: Lab: BIOS_CNTL Testing
Re-run write_bios_deadbeef.sys with OSR Driver Loader
Now we’ll successfully write 0xdeadbeef to the base of the BIOS region at FLA 0x260000
Run Copernicus.bat to dump the flash contents
Open Copernicus_BIOS.bin in the C:\ drive and go to address 0x260000
*You can just keep HxD open with the Copernicus_BIOS.bin file loaded, it will overwrite

## Slide 70: Lab: BIOS_CNTL Testing
Run reset_bios_FFFFFFFF.sys with OSR Driver Loader
This will write 0xFFFFFFFF to the base of the BIOS region at FLA 0x260000, thus resetting the original value there
Run Copernicus.bat to dump the flash contents
Open Copernicus_BIOS.bin in the C:\ drive and go to address 0x260000
Verify that 0xFFFFFFFF is back at flash address 0x260000

## Slide 71: Lab: BIOS_CNTL Testing
You don’t have to do this, but note that it is possible to set BIOS Lock Enable to 1 and not have an SMI handler routine running that checks and de-asserts BIOS Write Enable bit 0
We've seen this on multiple systems; where BLE was set, but asserting BIOSWE to 1 was not reset to 0
This is why bit 0 must be tested in order to really test write-protection

## Slide 72: vulnBIOS specific: BIOS_CNTL Testing: Set BLE
Now we’re going to setup BIOS_CNTL so that it protects the flash
This will only work on these lab machines with this modified BIOS
I inserted a custom SMI handler that resets the BIOSWE bit to 0 if it is asserted
We’re going to enable this by writing the word 0xb105 to port 0xB2
You should now see the BLE bit asserted in BIOS_CNTL (0x0A)

## Slide 73: vulnBIOS specific: BIOS_CNTL Testing
Now try to enable writes to the BIOS by asserting BIOSWE bit 0
  Set BIOS_CNTL to 0x0B
You will notice that it resets to 0x0A
This is the SMI handler working as it should
Note the reset of BIOSWE to 0 occurs during SMM
Any tangible delay you see in resetting this value is due to the (configurable) “Refresh” button in RW-E
Bit 0 is de-asserted

## Slide 74: BIOSWE/BLE should be considered deprecated!
We can defeat it on systems that are not using SMRRs
  "The Sicilian" – "Defeating Signed BIOS enforcement", Kallenberg et al., EkoParty 2013
We can defeat it on systems that don't set SMI_LOCK
  "Charizard" – "Setup for Failure: Defeating UEFI Secure Boot", Kallenberg et al., Syscan 2014
  But Charizard actually found by Sam Cornwell, it just got merged into Corey's talk in its first appearance. Will be spun off later.
We can defeat it on systems TXT-enabled that suppress SMIs
  "Sandman" – "SENTER Sandman: Using Intel TXT to attack BIOSes", Kovah et al., Summercon 2014
We have a new fundamental attack against it that will break it on all systems, once and for all. Targeted for this Dec.

## Slide 75: BIOS_CNTL: SMM_BWP
In PCH chipsets, bit 5 of BIOS_CNTL has been defined:
Provides the vendor the ability to ensure that BIOS region may ONLY be written to when all processors are in SMM and BIOSWE is enabled
Our lab system does not implement this bit because it is an MCH/ICH system, but check it out on your own
As we’ve seen, this register is important to lock down the BIOS to mitigate SMI suppression
Same here
Only 6 out of ~10k systems we’ve measured to date use it!!! 
  As of 3/31/2014

## Slide 76: Another Protection Mechanism
BIOS Range Write-Protection is the second major line of defense
There are 5 Protected Range registers (0-4) with independent R/W permissions
Setting these will prevent reads and/or writes until the system is reset.
* Information on FWH Sector Protection is hard to come by. It appears to be a security mechanic on the chip itself, since chips can be described as being divided into sectors.

## Slide 77
Example of a Protect Range Register
So who protects
the protector?
This guy that’s who
Notes: Move to after we cover the FD and the flash masters

## Slide 78: Protected Range (PR) Registers
The protections prescribed herein are enforced even upon the SMI handler
Enforced on register access, not direct access, however
Protected ranges are available to an SPI flash operating in either Non-Descriptor mode or Descriptor mode
  The ranges don’t have to mirror descriptor mode regions
Base addresses must be page-aligned
  Lower 12 bits are 000h
Limit addresses end at one under a page aligned boundary
  Lower 12 bits are FFFh
Addresses are Flash Linear Addresses (FLAs)
  Basically an offset from the base of the flash
  So “offset” 0x260000 on the flash is Flash Linear Address 0x260000

## Slide 79: PR Sample: Base 2A2000h
To set a PR from a Flash Linear Address Limit:
PRbase = ((page-aligned FLAbase) & FFF000) >> 12
PRbase |= 2A2 = 0000002A2h
To write-protect this range: PR0 | = 80000000h
To read-protect this range: PR0 |= 00008000h
*We’re picking a funny base because the offset at the real BIOS base is normally all 0xFF’s so it’s harder to illustrate the point.
This example will show us a visible boundary whereas the real BIOS base address would not.
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
WP |  |  | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | R P |  |  | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0
24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
FLAbase = 2A2000h
Protected Range Base

## Slide 80: PR Example: Limit 3FFFFFh
To set a PR from a Flash Linear Address Limit:
PRlimit = (page-aligned FLAlimit) << 16
PRlimit = 3FF000 << 4 = 03FF02A2h
To write-protect this: PR | = 80000000h
To read-protect this: PR |= 00008000h
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
WP |  |  | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | R P |  |  | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0
24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
FLAlimit = 3FFFFFh
Protected Range Limit

## Slide 81: Lab: Protected Range Registers
On our lab E6400, the BIOS region occupies the range 260000 – 3FFFFFh on the physical chip
  260000h and 3FFFFFh are Flash Linear Addresses (FLAs)
The CPU/BIOS (including us using RW-E) always has Read/Write access the BIOS region on flash
  Per the flash master permission settings
BIOS Region
260000h (start of BIOS region)
3FFFFFh (BIOS limit)

## Slide 82: Lab: Protected Range Registers
The previous slides set up a protected range from 2A2000h to 3FFFFFh
PR = 03FF02A2h (has not yet been read/write protected)
On our lab machines, this covers a portion of our BIOS region
BIOS Region
2A2000h (start of protected range)
260000h (start of BIOS region)
3FFFFFh (BIOS limit)

## Slide 83: Lab: Protected Range Registers
Let’s first verify we can read this by viewing the BIOS dump from Copernicus
PR = 03FF02A2h (has not yet been read/write protected)
On our lab machines, this covers a portion of our BIOS region
BIOS Region
2A2000h (start of protected range)
260000h (start of BIOS region)
3FFFFFh (BIOS limit, end of protected range)

## Slide 84: Lab: Protected Range Registers
First let’s establish that we have permission to read the BIOS region
Run Copernicus and open the .bin file with your favorite hex editor (HxD is a good one for Windows)
Observe binary range 2A2000-3FFFFFh
Looks like BIOS to me!
2A2000h (PR Start)
3FFFFFh (PR End (BIOS Limit))
.
.
.
.
.
.
.
.
.

## Slide 85: Lab: Protected Range Registers
To Write-protect a range:
PR | = 80000000h
To Read-protect a range:
PR |= 00008000h
For this example let’s disable reads to this range:
Set PR0 (at SPIBAR + 74h) to 03FF82A2h

## Slide 86: Lab: Protected Range Registers
Now re-run Copernicus and view the BIOS binary file in a hex editor
As you can see the Protected Range registers override the Flash Master permissions
This is the BIOS region to which the CPU/BIOS Master otherwise “always” has permission to read and write
2A2000h (PR Start)
3FFFFFh (PR End (BIOS Limit))
.
.
.
.
.
.
.
.
.

## Slide 87: Experiment: Overlapping PR Ranges
What happens when two (or more) protected ranges overlap with differing permissions?
This test will experiment with the following two (typically) adjacent regions which the CPU/BIOS typically has R/W access to
  Gigabit Ethernet: 1000 – 2FFFh
  Platform Data: 3000h - AFFFh
3000h (Platform Data region base)
1000h (Gigabit Ethernet region base)
AFFFh (Platform Data region limit)

## Slide 88: Experiment: Overlapping PR Ranges
As said, the CPU/BIOS has R/W permissions to both of these
We’ll disable writes to the Gigabit Ethernet region to make it read-only
We’ll disable reads to the Platform Data
3000h (Platform Data region base)
1000h (Gigabit Ethernet region base)
AFFFh (Platform Data region limit)

## Slide 89: What if the PR Limit Overruns the Flash Chip Limit?
The CPU/BIOS has read permissions to the BIOS region whose limit equals the physical limit (size) of the flash
The CPU/BIOS also has read permissions to the Flash Descriptor which is located at the base of the flash
What happens when we set a protected range that extends beyond the limit of the flash?
Is it ignored? Does the flash controller “wrap it around” to the front of the flash?
300000h (BIOS region base)
400FFFh (PR limit)
0FFFh (Flash Descriptor limit)
3FFFFFh (BIOS region limit)
?

## Slide 90: Experiment: PR Limit Overruns Flash Chip Limit
To test this we’ll disable reads to the following range:
base = 300000h limit = 400FFFh
PR0 = 04008300h
Ensure other PR’s are zero

## Slide 91: Experiment: PR Limit Overruns Flash Chip Limit
Once set, run Copernicus (or other flash –dumping tool), and view the results
We are still able to read the Flash Descriptor region
As expected, the BIOS is unreadable
Readable
Not Readable

## Slide 92: Experiment: PR Limit Overruns Flash Chip Limit
Therefore, the upper portion of the protected range that extends past the end of the flash is simply ignored
It does not wrap around to the front of the flash
Also of importance is knowing that the permissions are still applied to the valid parts of the range and aren’t “thrown out” because it is technically an invalid range
Not terribly surprising, but good to know!
300000h (BIOS region base)
400FFFh (PR limit)
0FFFh (Flash Descriptor limit)
3FFFFFh (BIOS region limit)

## Slide 93: PR Summary:
Implementing Protected Ranges is an important strategy for locking down a system BIOS
Without PR’s, any bypass of SMM’s global write-protection means an attacker is automatically able to modify the BIOS
Protected Range register enforcement:
  Overrides the Flash Master permissions
  Prevents Reads/Writes directly from the flash, even when the processor is running in SMM
    We did not demonstrate this, but it is true
Because of this, BIOS updates (or updates to protected ranges) must be performed using the capsule-update method before the Protected Ranges are configured by the BIOS
Only the vendor can reliably configure PR’s since new UEFI BIOS’ use the flash as a file system

## Slide 94: BIOS Base Address Configuration Register (BBAR)
This register prevents SPI commands (read/write/erase) from occurring below the specified address; including memory reads
Similar to a PR register
Tested on my system and register bits are read-only
  Attributes could be Write-Once, RO thereafter (typo?)
Typo: describes a different register 
The offset might also be a typo: register appears to be read-only
The first and last time you'll be seeing Babar
Notes: Wish I could talk more about this one but I can’t test it
http://imagopole.info/img/babar/5.jpeg

## Slide 95: Flash Region Access Permissions (FRAP)
The BIOS master may grant the GbE and/or the ME masters Write and/or Read access to the BIOS’ region
Bits 15:0 are always Read-Only
Contents will reflect the permissions configured in the FLMSTR1 (CPU/BIOS) register. however if another flash master has provided more permissive permissions to the CPU/BIOS, then that additional permissive bit will be reflected here as well
Descriptor Mode Only!
Notes: http://2.bp.blogspot.com/-Ov11wliyk4o/UHVhYVBS2EI/AAAAAAAABm4/rZio72_x_lw/s1600/Salted+Caramel+Mocha+Frappuccino.jpg

## Slide 96: FRAP Flash Descriptor Security
Bits 15:0 of FRAP will override the access permissions defined in the flash descriptor if this FDOPSS bit is 0
The HDA_SDO signal is not a soft-strap, it is a physical strap and cannot be changed programmatically
We have not seen a system on which the FDOPPS is asserted, so testing has been limited
Descriptor Mode Only!

## Slide 97: FRAP Example (not a lab*)
Tested by disabling CPU/BIOS write access to the GbE region in the FLMSTR1 register (in the flash descriptor)
  New FLMSTR1 value: 121B0000h
  Reflected in FRAP register bits 15:0 as 0000121Bh
Only possible to test if you can write to your Flash Descriptor
  Which you should not be able to do; I used an EEPROM programmer
*Requires modifying the flash descriptor which is Read-Only in this class to prevent the “easy-brick oven”

## Slide 98: FRAP Example
Set FRAP in the GbE BAR to permit write access to the CPU/BIOS (02020808h)
Yes, the GbE master also has it’s own flash program registers to configure and lock down
Located at memory-mapped address MBARB
  GbE LAN device (D25:F0), Offset 14h
  On class E6400, MBARB is at F6FD_B000h
FRAP
GbE SPI Flash Program Registers Base (MBARB)
SPIBAR
MBARB
At this point the graphics are probably jumping the shark? From clever to contrived?

## Slide 99: FRAP Example
Modified GbE FRAP to provide write-access to the CPU/BIOS (that which had been disabled in CPU/BIOS flash master
Bit 25 of GbE FRAP determines whether the CPU/BIOS master has write-permission to the GbE region of flash

## Slide 100: FRAP Example
As a result of modifying the GbE FRAP register to grant write access to the CPU/BIOS master
This change is reflected in the CPU/BIOS FRAP register indicating the write-access permission to GbE region
Now the CPU/BIOS can write to the GbE region
Note: The GbE master could not remove CPU/BIOS write-access to the GbE region if the CPU/BIOS FLMSTR1 register grants write-access to that region (same for all masters)

## Slide 101: FLOCKDN Register
Up to now we’ve been able to easily modify (and re-modify) registers in the SPI configuration registers that are designed to protect the system
For example, we can configure and modify the protected range registers to suit the needs of a lab
But if we can change them, so can any other app capable of mapping SPIBAR
Therefore they don’t really provide a lot of protection do they?
Intel provides the FLOCKDN register to solve this problem
Available in Descriptor mode and Non-Descriptor mode*
  Also called the “SPI Configuration Lock-Down” bit
  Also called the “Flash Configuration Lock-Down” bit
*I have not found this explained anywhere, I had to determine this through testing.
Notes: He who watches the watcher … FLOCKDN

## Slide 102: FLOCKDN
FLOCKDN, when asserted, prevents certain configuration registers/bits in the SPI BAR from being changed
Once asserted, FLOCKDN cannot be reset to 0 until a reset
Although hardware-sequencing is available only in descriptor mode, the FLOCKDN bit still provides register lock-down protection when the flash is operating in non-descriptor mode
  Called SPI or Flash Configuration Lock-Down bit

## Slide 103: FLOCKDN Affected Registers:
Flash Regions Access Permissions Register (FRAP)
  bits 31:24 (BMWAG) and bits 23:16 (BMRAG)
Protected Range (PR) registers 0 to 4
  entire register is locked
Software Sequencing Flash Control Register (SSFC)
  bits 18:16
  Configure SPI Cycle Frequency (20 MHz, 33 MHz, or 50 MHz [PCH only])
Prefix Opcode Configuration Register (PREOP)
  entire register is locked
Opcode Type Configuration Registers (OPTYPE)
  Entire register is locked
Opcode Menu Configuration Register (OPMENU)
  Entire register is locked

## Slide 104: FLOCKDN Testing*
I tested whether FLOCKDN locks down registers even when the chip is operating in non-descriptor mode (it does)
I tested this by corrupting the flash descriptor, thus putting the system in Non-Descriptor mode upon reboot
I tested changing the PREOP register (SPIBAR + 94h) which is normally R/W
I then asserted FLOCKDN bit 15 in HSFS
I again tested changing the PREOP register (SPIBAR + 94h) and found that I was not able to
I then tested writes to PR0 and also found that although the system was in non-descriptor mode, the PR registers were still locked as well
*Not available as a lab right now because my software sequencing SPI routine is broken

## Slide 105: GbE SPI Flash Program Registers
The Gigabit Ethernet master also has some programming registers as well
  Not as many as CPU/BIOS
Mirror those of the CPU/BIOS which we have been discussing
We won’t discuss them since it’s redundant, but those marked should be configured similarly to those of the CPU/BIOS SPI programming registers
*FRAP will only need modification if you are providing R/W access to another Master
MBARB

## Slide 106: SPI Lockdown Summary 1
Locking down the SPI Flash is a little more complicated than locking down SMM
For the most part, only the vendor can do this, but you can verify and try to implement some yourself
Verify that BIOS_CNTL.BLE is set
  If it’s not set, you can assert it yourself but that doesn’t mean there is SMI handler code present that will de-assert bit 0
Verify that SMM is protecting the BIOS from writes by asserting bit 0 and ensuring that it is reset
If supported, ensure that SMM BIOS Write Protect Disable (in the BIOS_CNTL register) is asserted so that the BIOS can only be written to when the processor is in SMM
  You can set this yourself. The only drawback being that you may not be able to update the BIOS, depending on how the vendor implemented updates

## Slide 107: SPI Lockdown Summary 2
Verify that Protected Range registers are being used
  You could also set these yourself but it will be a trial and error exercise since you won’t know what parts of the BIOS flash will be used to store variables (UEFI definitely and some Legacy)
Set FLOCKDN to ensure the above registers can’t be changed
The above changes you could play with won’t permanently hurt your system if they lock it up – they will all reset back to their original values on startup
Verify that the Flash Master permissions are set and that the Flash Descriptor region cannot itself be written to
  You have no control over this unless it is writeable, in which case the most you should do is make the FD un-writeable
  Messing with this one could brick your system “permanently”

## Slide 108: SPI Summary
Locking down the SPI flash memory is the first line of defense against an attacker
It is complicated and hard for vendors to get right
It gets a little more complex in UEFI where the SPI flash is specifically used as a file system for storing system variables
  Can’t just set a single PR to write-protect the whole BIOS region
Remember:
The BIOS boots from the flash and is responsible for configuring all of the settings we have been discussing so far in the class
Letting an attacker modify the BIOS means game over
It’s not easy, but it’s not that hard either for an attacker to modify your BIOS flash

## Slide 109: SPI Summary
All the settings in this section apply to both x86 and x64 architecture
All the settings in this section apply to both legacy BIOS and UEFI BIOS
All the settings in this section apply to systems running legacy MCH/ICH chipsets and the new PCH chipsets
  Except where otherwise noted (SMM_BWP)

## Slide 110: But wait there’s more!
Rollback attacks
  “Updates” (optional discussion)
How the vendor can protect against this:
  Firmware Signing
  Secure Boot (basically firmware signing in regards to the flash installation)
However, software bugs can bypass ALL of the above protections
  Wojtczuck & Tereshkin bypass firmware signing (2009)
    http://invisiblethingslab.com/resources/bh09usa/Attacking%20Intel%20BIOS.pdf
  Kallenberg et al. bypasses firmware signing (2013)
    https://media.blackhat.com/us-13/US-13-Butterworth-BIOS-Security-Slides.pdf
  Kallenberg et al. bypasses firmware signing (2 ways) (2014)
    BlackHat USA 2014

## Slide 111: Flash BIOS Exploits
Updates and vulnerabilities related to attackers being able to control variables parsed by SMM and/or BIOS during the update or boot process
BIOS is complicated and hard to debug
At some point, the operating system in one way or another has an opportunity to “interact” with the BIOS
  Not directly, but through proxy (like SMM maybe) to update the BIOS for example
This can be seen during the update process on all systems and also in with UEFI variables
First we’ll talk about the update process, briefly

## Slide 112: BIOS Updates

## Slide 113: NIST 800-155 Update Methods
Where NIST 800-147 describes ways to initialize the BIOS update process, NIST 800-155 describes ways that the system should actually perform the update
None: The flash BIOS cannot be updated
  This could mean that the SPI Flash is simply not writeable or
  There is no software update mechanism
Capsule: from the OS the BIOS image is written to RAM; a soft reboot is performed; the BIOS (preferably SMM) updates the BIOS following the reboot
System Management Mode (SMM): from the OS the BIOS image is written to RAM and then an SMI is triggered at which point an SMI handler performs the BIOS update
  Permits the OS to continue running after the update although the features of the new BIOS will not be enabled until the next reboot
Other

## Slide 114: Capsule Update: User Space
$RPK… Packet=1, size=0x400
Copyright 2011 Dell Inc.. A29
$RPK… Packet=N, size=0x100
EB 39 00 00 00 FF FF FF FF …
$RPK… Packet=2, size=0x1000
00 00 FF FF FF FF FF…
Kernel Driver
OEM update
utility
Privileged user executes the vendor-provided update utility
“Packetizes” BIOS image in RAM
Flips CMOS bit to signal BIOS that a firmware update is present
(There are other ways the BIOS could be made aware of a pending update on reboot, but this works just fine)
“Soft” reboots system
Dell E6400 example

## Slide 115: Capsule Update: Upon Reboot
SMM BIOS Update Routine
$RPK… Packet=N, size=0x100
00 00 FF FF FF FF FF…
$RPK… Packet=N-1, size=0x1000
EB 39 00 00 00 FF FF FF FF FF …
Image Reconstruction Space:
Copyright 2011 Dell Inc. A29..
00 00 FF FF FF FF FF …
…
EB 39 00 00 FF FF FF FF FF FF
BIOS Chip
Reconstructs BIOS Image
Verifies
signature!
System Management Mode RAM
The SMI handler reconstructs the image
If signed firmware updates are enabled, the signature is verified

## Slide 116: Capsule Update: Upon Reboot
SMM BIOS Update Routine
$RPK… Packet=N, size=0x100
00 00 FF FF FF FF FF…
$RPK… Packet=N-1, size=0x1000
EB 39 00 00 00 FF FF FF FF FF …
Image Reconstruction Space:
Copyright 2011 Dell Inc. A29..
00 00 FF FF FF FF FF …
…
EB 39 00 00 FF FF FF FF FF FF
BIOS Chip
Reconstructs BIOS Image
System Management Mode RAM
If the image signature is valid (or perhaps a checksum if firmware signing isn’t being used), the SMI handler writes the image to the flash.
Flashes
BIOS!

## Slide 117: Capsule Update Process Summary
The previous example assumes a signed firmware check
Without requiring firmware signing, typically the only integrity check a BIOS must pass is that of a checksum
  In other words, only an integrity check against mal-formation
  Not security
The previous example also takes into account that Dell breaks up their firmware image into packets and then reconstructs it upon reboot
  That is tough hand-coded assembly to write!

## Slide 118: SMM Update: User-Space
BIOS Update Image
Kernel Driver
OEM update
utility
Privileged user executes the vendor-provided update utility
BIOS image is written to RAM
SMI is triggered to signal SMM that a firmware update is pending
In this example the binary is not in packets but is a flat image (seen both, either is valid)
Dell E6400 example
System Management Mode RAM

## Slide 119: SMM Update: SMM
SMI Handler Updates BIOS
BIOS Chip
SMI Handler verifies and updates BIOS
System Management Mode RAM
BIOS Update Image
Signature is checked if enabled
Otherwise may just be a checksum (not secure)
Verifies
signature!

## Slide 120: SMM Update: SMM
SMI Handler Updates BIOS
BIOS Chip
SMI Handler verifies and updates BIOS
System Management Mode RAM
BIOS Update Image
BIOS Flash is updated by SMI handler
Control can be returned to OS without reboot
New configuration won’t be realized until next reboot
Flashes
BIOS!

## Slide 121: Protecting BIOS from Malicious Updates
There’s nothing preventing an attacker from researching how a system performs its updates
  Copy image to memory
  Determine what sort of update pending flag the BIOS update process uses
    CMOS bit, etc.
  Set that update flag
What prevents an attacker from doing this?
Firmware signing

## Slide 122: Firmware Signing – almost perfect
Signed firmware updates requires that only an authorized BIOS (signed by a trusted authority) can be flashed to the chip
However, it has no capability to protect against bootkits installed after-the-fact, like that from an Evil Maid attack
Microsoft BitLocker will prevent this specific attack assuming it's used with the TPM and the TPM Platform Configuration Registers change due to the modified MBR
  However, BitLocker won’t protect against malicious PCI Option ROMs, etc, unless they're being properly measured too
UEFI Secure Boot will also prevent this malicious MBR from executing because it will have failed the firmware signature check
Therefore, firmware signing in conjunction with secure boot (or TPM-enabled BitLocker) provides good protection
  More about Secure Boot and TPM later

## Slide 123: Firmware Signing & Rollback Attacks
One thing to remember is that OEMs generally allow you to also downgrade a BIOS
So if an attacker knows BIOS revision X is vulnerable, they may be able to downgrade the BIOS to that vulnerable revision
The vendor can prevent this by revoking signing keys
  The BIOS firmware contains a key store of approved signing key(s)
An example of the revocation process:
  A vendor releases a BIOS update with it’s key store containing only the new sign key
  All the customer has to do is update their BIOS and they are “baselined” to the new revision

## Slide 124: Software Vulnerabilities Trump All…
Signed firmware updates are very good; they prevent an attacker from being able to easily update a system BIOS with a malicious image
However, even with firmware signing enabled, vulnerabilities in the code can still allow an attacker to gain entry to the system
“Attacking Intel BIOS” by Rafal Wojtczuk and Alexander Tereshkin
  Bypassed firmware signing by exploiting a vulnerability in the code that parses the BIOS splash image
Or ours :)
VU #552286 coming soon!

## Slide 125: BIOS Exploits
BIOS is firmware.
Firmware is software.
Software can be vulnerable.
Therefore BIOS can be vulnerable.
Vulnerable BIOS can be exploited.

## Slide 126: Dell Capsule Update: User Space
$RPK… Packet=1, size=0x400
Copyright 2011 Dell Inc.. A29
$RPK… Packet=N, size=0x100
EB 39 00 00 00 FF FF FF FF …
$RPK… Packet=2, size=0x1000
00 00 FF FF FF FF FF…
Kernel Driver
OEM update
utility
“Packetizes” BIOS image in RAM
Flips CMOS bit to signal BIOS that a firmware update is present
“Soft” reboots system

## Slide 127: Dell Capsule Update: BIOS, on Reboot
SMM BIOS Update Routine
$RPK… Packet=N, size=0x100
00 00 FF FF FF FF FF…
$RPK… Packet=N-1, size=0x1000
EB 39 00 00 00 FF FF FF FF FF …
Image Reconstruction Space:
Copyright 2011 Dell Inc. A29..
00 00 FF FF FF FF FF …
…
EB 39 00 00 FF FF FF FF FF FF
BIOS Chip
Update Firmware
Reconstructs BIOS Image
Verifies
signature!
System Management Mode RAM

## Slide 128: Attack Surface ($RPK)
http://linux.dell.com/libsmbios/main/RbuLowLevel_8h-source.html
Notes: This is the attack surface; data which the attacker controls.

## Slide 129: BIOS Update: Locate & Parse Packet
Update process scans memory for the $RPK string.
Once located, packet data members are stored in an SMM data area for use in later calculations…

## Slide 130: BIOS Update: Curious GEOR?
The reconstruction area is populated with ‘GEOR’ at page-aligned boundaries
‘GEOR’ must be present at the location where packet payload is to be written

## Slide 131: BIOS Update: Copy Packet
Notice the size parameter (ecx) for the inline memcpy (rep movsd) is derived from attacker controlled data (g_pktSizeMinusHdrSize)
ECX controls the number of dwords copied in the rep movsd instruction
Notes: And that’s not the only attacker controlled data

## Slide 132: More Attacker Controlled Data
In fact, the source and destination are also both derived from attacker controlled data.
This is an exploitable buffer overflow.

## Slide 133: A “Constraints Solving” Problem
Source, Destination, and Size have dependencies
  Changing one operand, changes the others.
Plus, other constraints must be accounted for:
  Our copy destination must point to an area pre-initialized with ‘GEOR’.
  Copy_dest must be lower in memory than the return address.
  We can’t overwrite too much lest we die in the inline memcpy and never return.

## Slide 134: ‘Evil’ Packet Solution
With all those constraints in mind, we brute force a packet configuration that allows us to pass the sanity checks and overwrite the return address gracefully.

## Slide 135: ‘Evil’ BIOS Update: User Space
‘Evil’ Kernel Driver
‘Evil’ Binary
Only has to write a single packet
Writes ‘GEOR’ at packet destination
Flips CMOS bit to signal BIOS that a firmware update is present
“Soft” reboots system
$RPK.. Packet=0x83f9, size=0xfffe
Shellcode
Shellcode
…
Shellcode
‘GEOR’

## Slide 136: ‘Evil’ BIOS Update: Upon Reboot
BIOS Chip
SMM BIOS Update Routine
System Management Mode RAM
Reconstructs BIOS image exploiting buffer overflow
Image Reconstruction Space:
Shellcode
Shellcode
….
Shellcode
$RPK.. Packet=0x83f9, size=0xfffe
Shellcode
Shellcode
…
Shellcode
Overflows
function Return;
controls EIP!

## Slide 137: PoC Demonstration Video http://youtu.be/V_ea21CrOPM

## Slide 138: BIOS Exploit Summary
This example was performed on a legacy BIOS
UEFI BIOS is also vulnerable, as you will see
BIOS is buggy, like all software
It’s hard to write code like this that parses complex images
  Hard enough to get it working
If an attacker could control a variable at any point, that variable must be validated thoroughly
Attackers may have all the time in the world to investigate the binaries for vulnerabilities