## Slide 1: Introduction to Intel x86-64 Assembly, Architecture, Applications, & Alliteration
Xeno Kovah – 2014-2015
xeno@legbacore.com

## Slide 2
All materials is licensed under a Creative Commons “Share Alike” license.
http://creativecommons.org/licenses/by-sa/3.0/
Attribution condition: You must indicate that derivative work
"Is derived from Xeno Kovah's 'Intro x86-64’ class, available at http://OpenSecurityTraining.info/IntroX86-64.html”
Notes: Attribution condition: You must indicate that derivative work
"Is derived from Xeno Kovah's ‘Intro x86-64’ class, available at http://OpenSecurityTraining.info/IntroX86-64.html"

## Slide 3
MulDivExample.c
int main(){
unsigned int a = 1;
a = a * 6;
a = a / 3;
return 0x2bad;
}
main:
0000000140001010 sub rsp,18h
0000000140001014 mov dword ptr [rsp],1
000000014000101B mov eax,dword ptr [rsp]
000000014000101E imul eax,eax,6
0000000140001021 mov dword ptr [rsp],eax
0000000140001024 xor edx,edx
0000000140001026 mov eax,dword ptr [rsp]
0000000140001029 mov ecx,3
000000014000102E div eax,ecx
0000000140001030 mov dword ptr [rsp],eax
0000000140001033 mov eax,2BADh
0000000140001038 add rsp,18h
000000014000103C ret
Notes: We already saw that when a C operand is a power of 2, it uses shifts instead of multiplies/divides, but this shows that in other cases, it uses multiply or divide instructions.

## Slide 4
DIV - Unsigned Divide
Three forms
  Unsigned divide ax by r/m8, al = quotient, ah = remainder
  Unsigned divide edx:eax by r/m32, eax = quotient, edx = remainder
  Unsigned divide rdx:rax by r/m64, rax = quotient, rdx = remainder
If dividend is 32/64bits, edx/rdx will just be set to 0 by the compiler before the instruction (as occurred in the MulDivExample.c code)
If the divisor is 0, a divide by zero exception is raised.
27
ax | r/m8(cx)
0x8 | 0x3
ah | al
0x2 | 0x2
div ax, cx
edx | eax | r/mX(ecx)
0x0 | 0x8 | 0x5
edx | eax | r/mX(ecx)
0x3 | 0x1 | 0x5
div eax, ecx
initial
operation
result
Book page 69
Notes: Note that there’s no form which takes an immediate.

## Slide 5
IDIV - Signed Divide
If you were to then change MulDivExample to signed, you would see the IDIV instruction appear
Three forms
  Signed divide ax by r/m8, al = quotient, ah = remainder
  Signed divide edx:eax by r/mX, eax = quotient, edx = remainder
  Signed divide rdx:rax by r/m64, rax = quotient, rdx = remainder
If dividend is 32/64bits, edx/rdx will just be set to 0 by the compiler before the instruction
If the divisor is 0, a divide by zero exception is raised.
28
ax | r/m8(cx)
0xFE | 0x2
ah | al
0x0 | 0xFF
div ax, cx
edx | eax | r/mX(ecx)
0x0 | 0x8 | 0x3
edx | eax | r/mX(ecx)
0x1 | 0x2 | 0x3
div eax, ecx
initial
operation
result
Book page 69
Notes: Note that there’s no form which takes an immediate.

## Slide 6
MulDivExample.c takeaways
int main(){
unsigned int a = 1;
a = a * 6;
a = a / 3;
return 0x2bad;
}
main:
0000000140001010 sub rsp,18h
0000000140001014 mov dword ptr [rsp],1
000000014000101B mov eax,dword ptr [rsp]
000000014000101E imul eax,eax,6
0000000140001021 mov dword ptr [rsp],eax
0000000140001024 xor edx,edx
0000000140001026 mov eax,dword ptr [rsp]
0000000140001029 mov ecx,3
000000014000102E div eax,ecx
0000000140001030 mov dword ptr [rsp],eax
0000000140001033 mov eax,2BADh
0000000140001038 add rsp,18h
000000014000103C ret
When a multiply or divide is not by a power of 2, compilers will use normal multiply/divide instructions
VS compiler prefers IMUL over MUL (unsigned multiply) for simple multiplies, due to its option to use 3 parameters
Notes: We already saw that when a C operand is a power of 2, it uses shifts instead of multiplies/divides, but this shows that in other cases, it uses multiply or divide instructions.

## Slide 7
Instructions we now know (28)
NOP
PUSH/POP
CALL/RET
MOV
ADD/SUB
IMUL
MOVZX/MOVSX
LEA
JMP/Jcc (family)
CMP/TEST
AND/OR/XOR/NOT
INC/DEC
SHR/SHL/SAR/SAL
DIV/IDIV