## Slide 1: Introduction to Intel x86-64 Assembly, Architecture, Applications, & Alliteration
Xeno Kovah – 2014-2015
xeno@legbacore.com

## Slide 2
All materials is licensed under a Creative Commons “Share Alike” license.
http://creativecommons.org/licenses/by-sa/3.0/
Attribution condition: You must indicate that derivative work
"Is derived from Xeno Kovah's 'Intro x86-64’ class, available at http://OpenSecurityTraining.info/IntroX86-64.html”
Notes: Attribution condition: You must indicate that derivative work
"Is derived from Xeno Kovah's ‘Intro x86-64’ class, available at http://OpenSecurityTraining.info/IntroX86-64.html"

## Slide 3
ShiftExample0.c
void main()
{
unsigned int a, b, c;
a = 0x5;
b = a << 4;
c = b >> 3;
return c;
}
main:
0000000140001000 sub rsp,18h
0000000140001004 mov dword ptr [rsp],5
000000014000100B mov eax,dword ptr [rsp]
000000014000100E shl eax,4
0000000140001011 mov dword ptr [rsp+4],eax
0000000140001015 mov eax,dword ptr [rsp+4]
0000000140001019 shr eax,3
000000014000101C mov dword ptr [rsp+8],eax
0000000140001020 mov eax,dword ptr [rsp+8]
0000000140001024 add rsp,18h
0000000140001028 ret

## Slide 4
SHL - Shift Logical Left
Can be explicitly used with the C “<<” operator
First operand (source and destination) operand is an r/mX
Second operand is either cl (lowest byte of ecx), or a 1 byte immediate. The 2nd operand is the number of places to shift.
It multiplies the register by 2 for each place the value is shifted. More efficient than a multiply instruction.
Bits shifted off the left hand side are “shifted into” (set) the carry flag (CF)
For purposes of determining if the CF is set at the end, think of it as n independent 1 bit shifts.
 | 00110011b (bl - 0x33)
result | 11001100b (bl - 0xCC) CF = 0
shl bl, 2
21
 | 00110011b (bl - 0x33)
result | 10011000b (bl - 0x98) CF = 1
shl bl, 3
Book page 77-81

## Slide 5
SHR - Shift Logical Right
Can be explicitly used with the C “>>” operator
First operand (source and destination) operand is an r/mX
Second operand is either cl (lowest byte of ecx), or a 1 byte immediate. The 2nd operand is the number of places to shift.
It divides the register by 2 for each place the value is shifted. More efficient than a multiply instruction.
Bits shifted off the right hand side are “shifted into” (set) the carry flag (CF)
For purposes of determining if the CF is set at the end, think of it as n independent 1 bit shifts.
22
 | 00110011b (bl - 0x33)
result | 00001100b (bl - 0x0C) CF = 1
shr bl, 2
 | 00110011b (bl - 0x33)
result | 00000110b (bl - 0x06) CF = 0
shr bl, 3

## Slide 6
ShiftExample0.c Takeaways:
void main()
{
unsigned int a, b, c;
a = 0x5;
b = a << 4;
c = b >> 3;
return c;
}
main:
0000000140001000 sub rsp,18h
0000000140001004 mov dword ptr [rsp],5
000000014000100B mov eax,dword ptr [rsp]
000000014000100E shl eax,4
0000000140001011 mov dword ptr [rsp+4],eax
0000000140001015 mov eax,dword ptr [rsp+4]
0000000140001019 shr eax,3
000000014000101C mov dword ptr [rsp+8],eax
0000000140001020 mov eax,dword ptr [rsp+8]
0000000140001024 add rsp,18h
0000000140001028 ret
Shifts in C are shifts in asm :P

## Slide 7
ShiftExample1.c
#include <stdio.h>
#include <stdlib.h>
int main(int argc, char **argv)
{
unsigned int a, b, c;
a = atoi(argv[0]);
b = a * 8;
c = b / 16;
return c;
}
main:
0000000140001010 sub rsp,28h
0000000140001014 mov rcx,qword ptr [rdx]
0000000140001017 call qword ptr [40008368h]
000000014000101D shl eax,3
0000000140001020 shr eax,4
0000000140001023 add rsp,28h
0000000140001027 ret
Whither the multiply and divide instructions?!
Note: Compiled with “Maximize Speed”, to clear away a bit of cruft

## Slide 8
ShiftExample1.c takeaways
#include <stdio.h>
#include <stdlib.h>
int main(int argc, char **argv)
{
unsigned int a, b, c;
a = atoi(argv[0]);
b = a * 8;
c = b / 16;
return c;
}
main:
0000000140001010 sub rsp,28h
0000000140001014 mov rcx,qword ptr [rdx]
0000000140001017 call qword ptr [40008368h]
000000014000101D shl eax,3
0000000140001020 shr eax,4
0000000140001023 add rsp,28h
0000000140001027 ret
When a multiply or divide is by a power of 2, compilers prefer shift instructions as a more efficient way to perform the computation

## Slide 9
That’s the power of love sign!
#include <stdio.h>
#include <stdlib.h>
int main(int argc, char **argv)
{
unsigned int a, b, c;
a = atoi(argv[0]);
b = a * 8;
c = b / 16;
return c;
}
#include <stdio.h>
#include <stdlib.h>
int main(int argc, char **argv)
{
int a, b, c;
a = atoi(argv[0]);
b = a * 8;
c = b / 16;
return c;
}
Notes: http://4.bp.blogspot.com/-FAaWCtna3mw/Tc69R-mPbFI/AAAAAAAABxA/Nriylz_dc20/s1600/hlhlfr.jpeg

## Slide 10
ShiftExample2.c
#include <stdio.h>
#include <stdlib.h>
int main(int argc, char **argv)
{
int a, b, c;
a = atoi(argv[0]);
b = a * 8;
c = b / 16;
return c;
}
main:
0000000140001010 sub rsp,28h
0000000140001014 mov rcx,qword ptr [rdx]
0000000140001017 call qword ptr [40008368h]
000000014000101D shl eax,3
0000000140001020 cdq
0000000140001021 and edx,0Fh
0000000140001024 add eax,edx
0000000140001026 sar eax,4
0000000140001029 add rsp,28h
000000014000102D ret

## Slide 11
main:
0000000140001010 sub rsp,28h
0000000140001014 mov rcx,qword ptr [rdx]
0000000140001017 call qword ptr [40008368h]
000000014000101D shl eax,3
0000000140001020 shr eax,4
0000000140001023 add rsp,28h
0000000140001027 ret
Vs
Changed
CD* is added as an VS-ism. It’s necessary for the math to work out, but I feel like I’ve only run into it once ever in the wild. So I don’t consider it that important for beginners to know and I’m skipping it. But you can feel free to come back and read this code once we’ve gone through the RTFM section.
main:
0000000140001010 sub rsp,28h
0000000140001014 mov rcx,qword ptr [rdx]
0000000140001017 call qword ptr [40008368h]
000000014000101D shl eax,3
0000000140001020 cdq
0000000140001021 and edx,0Fh
0000000140001024 add eax,edx
0000000140001026 sar eax,4
0000000140001029 add rsp,28h
000000014000102D ret

## Slide 12
SAR - Shift Arithmetic Right
Can be explicitly used with the C “>>” operator, if operands are signed
First operand (source and destination) operand is an r/mX
Second operand is either cl (lowest byte of ecx), or a 1 byte immediate. The 2nd operand is the number of places to shift.
It divides the register by 2 for each place the value is shifted. More efficient than a multiply instruction.
Each bit shifted off the right side is placed in CF.
 | 10110011b (bl - 0xB3)
result | 00101100b (bl - 0x2C)
shr bl, 2
 | 10110011b (bl - 0xB3)
result | 11101100b (bl - 0xEC)
sar bl, 2
 | 00110011b (bl - 0x33)
result | 00001100b (bl - 0x0C)
 | 00110011b (bl - 0x33)
result | 00001100b (bl - 0x0C)
==
!=
23
mov cl, 2; sar bl, cl
mov cl, 2; shr bl, cl

## Slide 13
SAL - Shift Arithmetic Left
Actually behaves exactly the same as SHL!
First operand (source and destination) operand is an r/mX
Second operand is either cl (lowest byte of rcx), or a 1 byte immediate. The 2nd operand is the number of places to shift.
It divides the register by 2 for each place the value is shifted. More efficient than a multiply instruction.
Each bit shifted off the left side is placed in CF.
 | 10110011b (bl - 0xB3)
result | 11001100b (bl - 0xCC)
shl bl, 2
 | 10110011b (bl - 0xB3)
result | 11001100b (bl - 0xCC)
sal bl, 2
 | 00110011b (bl - 0x33)
result | 11001100b (bl - 0xCC)
mov cl, 2; sal bl, cl
 | 00110011b (bl - 0x33)
result | 11001100b (bl - 0xCC)
mov cl, 2; shl bl, cl
==
==
24

## Slide 14
ShiftExample2.c takeaways
int main(){
int a, b, c;
a = 0x40;
b = a * 8;
c = b / 16;
return c;
}
main:
0000000140001010 sub rsp,28h
0000000140001014 mov rcx,qword ptr [rdx]
0000000140001017 call qword ptr [40008368h]
000000014000101D shl eax,3
0000000140001020 cdq
0000000140001021 and edx,0Fh
0000000140001024 add eax,edx
0000000140001026 sar eax,4
0000000140001029 add rsp,28h
000000014000102D ret
Compilers still prefer shifts for mul/div over powers of 2
But when the operands are signed rather than unsigned, it must use different instructions, and potentially do more work (than the unsigned case) to deal with a multiply
CDQ isn’t important for beginners to know, left as an exercise for the reader for later ;)

## Slide 15
Instructions we now know (26)
NOP
PUSH/POP
CALL/RET
MOV
ADD/SUB
IMUL
MOVZX/MOVSX
LEA
JMP/Jcc (family)
CMP/TEST
AND/OR/XOR/NOT
INC/DEC
SHR/SHL/SAR/SAL