## Slide 1: Introduction to Intel x86-64 Assembly, Architecture, Applications, & Alliteration
Xeno Kovah – 2014-2015
xeno@legbacore.com

## Slide 2
All materials is licensed under a Creative Commons “Share Alike” license.
http://creativecommons.org/licenses/by-sa/3.0/
Attribution condition: You must indicate that derivative work
"Is derived from Xeno Kovah's 'Intro x86-64’ class, available at http://OpenSecurityTraining.info/IntroX86-64.html”
Notes: Attribution condition: You must indicate that derivative work
"Is derived from Xeno Kovah's ‘Intro x86-64’ class, available at http://OpenSecurityTraining.info/IntroX86-64.html"

## Slide 3
Digression – Why Two’s Compliment?
Alternative methods of representing negative numbers (signed magnitude, or just ones compliment), as well as their problems presented on page 166-167 of the 32 bit book.
  Note to self: show on board quick
The benefit of two’s compliment is due to having only one representation of zero, and being able to reuse the same hardware for addition/subtraction
Dave Keppler suggested expanding on this
46

## Slide 4
Why Two’s Compliment? 2
47
5d
+ 6d
11d
1
Carry
1b
+ 1b
10b
1
Table taken from
http://thalia.spec.gmu.edu/~pparis/classes/notes_101/node110.html

## Slide 5
Why Two’s Compliment? 3
48
XOR
AND
A half adder circuit suffices for one bit addition
Picture taken from
http://thalia.spec.gmu.edu/~pparis/classes/notes_101/node110.html

## Slide 6
Why Two’s Compliment? 4
49
Picture taken from
http://thalia.spec.gmu.edu/~pparis/classes/notes_101/node111.html
Full Adder
You can’t just chain the one bit half adders together to get multi-bit adders. To see why, see the truth table at the link.

## Slide 7
Why Two’s Compliment? 5
50
2 bit adder
Pictures taken from
http://thalia.spec.gmu.edu/~pparis/classes/notes_101/node112.html
http://thalia.spec.gmu.edu/~pparis/classes/notes_101/node113.html
4 bit adder
(continue to make n bit adder)
Note: we start with a half adder because a full adder would need a carry input at the start. However, if we wanted to use this for subtraction we could use a full adder to start. More on this on next slide.

## Slide 8
Why Two’s Compliment? 6
So you have these physical adder circuits in the Arithmetic Logic Unit (ALU), and you can feed both add and subtract to the same circuit. But for this to work, you need to start with a full adder, and then run one the one subtract operand bits through not gates, and then set carry to one on the first full adder.
Keppler’s example of x-y == x+(-y)
  Cause it was right there in my email and I’m lazy ;)
51
00001010 00001010 (10d) == 00001010 (10d)
+ 00000101 -00000101 (5d) +11111011 (-5d) ---------- --------- --------- 00001111 00000101 1 00000101